## Slide 1
Presidency University, Bengaluru
School of Artificial Intelligence and Advanced Computing
Department of AI & Robotics
Performance, Processor
Clock & Parallelism
Understanding how we measure, express, and improve computer performance
Computer Organization and Architecture | CSS2257
Manoj Sagar, Assistant Professor
Notes: Welcome students warmly. Introduce yourself and the subject: Computer Organization and Architecture, CSS2257. Tell them today's session answers a very practical question: when someone says 'this processor is fast,' what does that actually mean, and how do we measure and improve it? Mention that by the end of the hour they will be able to compute CPU execution time, apply Amdahl's Law, and explain why raw clock speed alone doesn't tell the whole story. Keep energy high and welcoming since this is a foundational, slightly math-heavy topic.

## Slide 2
Presidency University, Bengaluru
SCHOOL
School of Artificial Intelligence and Advanced Computing
DEPARTMENT
Department of AI & Robotics
COURSE
Computer Organization and Architecture (CSS2257)
FACULTY
Manoj Sagar, Assistant Professor
Notes: Briefly orient students to the institutional context. This helps freshers, especially in a large university, know exactly whose class they are in and which department is responsible for the course. Mention that CSS2257 is a core foundational course for understanding how computers actually work at the hardware and organizational level, and that today's topic feeds directly into later modules on pipelining and memory systems.

## Slide 3
Learning Objectives
Define computer performance in terms of response time and throughput
Compute CPU execution time using the Instruction Count, CPI, and Clock Cycle Time equation
Explain the processor clock: clock rate, cycle time, and their relationship
State and apply Amdahl's Law to evaluate the benefit of an enhancement
Describe key technology trends that have shaped modern processor design
Distinguish between instruction-level, data-level, and thread-level parallelism
Visual & Delivery Tip
Read each objective aloud. Tell students these are exactly the skills tested in today's quiz.
Presidency University, Bengaluru
CSS2257
Notes: Walk through each objective at a normal pace. Tell students: 'By the end of this class, you should be able to look at two processors' specifications and reason about which is actually faster, not just which has a bigger GHz number.' This sets clear expectations and gives them a mental checklist to track their own understanding as the lecture proceeds.

## Slide 4
Quick Icebreaker
Q1
When you buy a phone or laptop, what specification do you check first — GHz, RAM, or something else?
Q2
Have you ever noticed two phones with the 'same GHz' feeling very different in speed? Why do you think that happens?
Q3
If you could double just ONE part of your laptop to make it feel faster, what would you pick?
Presidency University, Bengaluru
CSS2257
Notes: Run this as a quick show-of-hands and open floor activity — don't spend more than 4 to 5 minutes here. Ask Q1 and take 2-3 quick verbal responses. For Q2, this is the key one: let 1-2 students describe their experience, and simply say 'hold that thought, we are going to explain exactly why that happens today.' Use their answers to segue: 'So clock speed alone clearly isn't the full story — today we find out what actually determines performance.'

## Slide 5
Why This Topic Matters
Every purchasing decision — phones, laptops, servers, GPUs — is ultimately a performance decision
Marketing numbers (GHz, core count) can mislead if you don't know how to interpret them
Architects use these exact formulas to decide whether a design change is worth the silicon area and power cost
Cloud companies pay per second of compute — understanding performance directly affects cost engineering
Visual & Delivery Tip
Show two real laptop spec sheets side by side to make the marketing-numbers point concrete.
Presidency University, Bengaluru
CSS2257
Notes: Connect the topic to real life immediately. Ask: 'Who here has argued with a friend about which phone is faster?' This is genuinely the content of today's class. Emphasize that engineers at companies like Intel, ARM, and Apple use precisely the formulas we are about to derive — this isn't abstract theory, it's the actual toolkit used in industry to make billion-dollar design decisions.

## Slide 6
What Do We Mean by “Performance”?
Performance is not a single fixed quantity — it depends on what you are measuring and for whom
Response Time (Latency)
Time between the start and completion of one task — matters to an individual user
Throughput (Bandwidth)
Total amount of work done per unit time — matters to a data-centre operator
Visual & Delivery Tip
Icons: stopwatch for response time, stacked bars for throughput. Fade in each definition in turn.
Presidency University, Bengaluru
CSS2257
Notes: Explain with an analogy: response time is how long it takes ONE car to drive from your home to college; throughput is how many cars per hour cross a toll booth. A racing car has great response time (fast for one trip); a well-designed highway with many lanes has great throughput (many cars per hour) even if no single car is exceptionally fast. Both matter, but for different audiences: you personally care about your own task finishing quickly, while a server administrator cares about total jobs completed per hour.

## Slide 7
Response Time vs. Throughput
Response Time
Start
Finish
One task, one user — minimize the elapsed time from start to finish.
Example: how long your video call app takes to load
Throughput
Many tasks, many users — maximize total work completed per unit time.
Example: number of transactions a bank server handles per second
Presidency University, Bengaluru
CSS2257
Notes: Point to the left card and trace the timeline with your hand: start dot, elapsed time, finish dot. Then move to the right card and point out the bars representing separate completed jobs. Ask a quick check-question: 'If I add a second checkout counter at a supermarket, does that improve response time for one customer, or throughput for the whole store, or both?' Let a student answer, then confirm: mainly throughput, since it doesn't speed up any single customer's checkout, but more customers get served per hour.

## Slide 8
Measuring Performance: CPU Execution Time
The most fundamental performance measure is CPU execution time — the time the CPU spends actually working on a program
It excludes waiting time for I/O or time-sharing with other programs
CPU time is influenced by three completely separate factors, controlled by different people: the compiler writer, the ISA designer, and the hardware engineer
CPU Time =
Instructions × Cycles/Instruction × Seconds/Cycle
Visual & Delivery Tip
Draw three interlocking gears — IC, CPI, Clock Cycle Time — to show they multiply together.
Presidency University, Bengaluru
CSS2257
Notes: Introduce the master formula students will use throughout the lecture and in the worked examples. Explain the three knobs separately: the number of instructions executed depends on the algorithm and compiler; the cycles needed per instruction depends on the instruction set and how the hardware implements it; and the time per cycle depends on the underlying circuit technology and clock design. Emphasize: to improve performance, you can attack any one of these three factors, and real engineering teams specialize in exactly one of them.

## Slide 9
Clock Cycles and Clock Rate
A processor's clock is an electronic signal that oscillates between high and low voltage at a fixed rate
Each tick of this signal is called a clock cycle (or clock tick)
Clock Rate (frequency) = number of cycles per second, measured in Hertz (Hz)
A 3.0 GHz processor completes 3 billion clock cycles every second
Clock Cycle Time = 1 / Clock Rate — the duration of a single cycle
One Clock Cycle
Visual & Delivery Tip
Highlight one full high-low cycle on the wave and label its duration as the Clock Cycle Time.
Presidency University, Bengaluru
CSS2257
Notes: Draw the square wave on the board too if helpful. Explain that every component inside the CPU — registers, ALU stages, control logic — is synchronised to this beat, similar to musicians following a metronome. Everyone in the orchestra (the different hardware units) acts on the same beat so their actions stay coordinated. State clearly: Clock Cycle Time and Clock Rate are reciprocals of one another; if you know one, you can compute the other by simple division.

## Slide 10
CPI — Cycles Per Instruction
Not every instruction takes the same number of clock cycles — a memory load may take more cycles than a simple addition
CPI = average number of clock cycles used per instruction, for a given program on a given machine
CPI depends on the instruction mix (what kinds of instructions the program actually uses) and the hardware implementation
If a program uses several instruction classes, overall CPI is the weighted average across all classes
Presidency University, Bengaluru
CSS2257
Notes: Give a concrete intuition: not all tasks in daily life take the same time — brushing your teeth is quick, cooking a meal takes longer. Similarly, an ADD instruction might finish in 1 cycle while a memory LOAD might need 4 cycles because it has to travel out to memory. CPI is simply the average, weighted by how often each instruction type appears in the program. Tell students we will compute this precisely in the next two slides with real numbers.

## Slide 11
Putting It Together — The Performance Equation
CPU Time = IC × CPI × Clock Cycle Time
IC
Instruction Count
Set by the algorithm & compiler
CPI
Cycles per Instruction
Set by the ISA & microarchitecture
CCT
Clock Cycle Time
Set by fabrication technology & circuit design
Presidency University, Bengaluru
CSS2257
Notes: This is the single most important equation of today's class — slow down and make sure everyone copies it down. Walk through each row: IC is decided far away from the hardware, by the algorithm and the compiler generating instructions; CPI is decided by how the instruction set is designed and how the pipeline executes it; Clock Cycle Time is decided by the fabrication process and circuit design, essentially the physics of the chip. Emphasize that these three are NOT independent in practice — improving one can sometimes worsen another, which is exactly why processor design is a balancing act, not a single-variable optimisation.

## Slide 12
Worked Example 1 — Computing CPU Time
A program runs 200 million instructions. The processor has CPI = 2 and a clock rate of 1 GHz. Find CPU time.
1
Identify knowns: IC = 200 × 10⁶, CPI = 2, Clock Rate = 1 × 10⁹ Hz
2
Find Clock Cycle Time: CCT = 1 / Clock Rate = 1 / (1×10⁹) = 1 nanosecond
3
Apply the formula: CPU Time = IC × CPI × CCT
4
Substitute: CPU Time = (200×10⁶) × 2 × (1×10⁻⁹) seconds
5
Compute: CPU Time = 400 × 10⁻³ s = 0.4 seconds
Presidency University, Bengaluru
CSS2257
Notes: Work through this on the board step by step, out loud, as shown on the slide. Point out the unit conversion carefully: gigahertz means 10^9 cycles per second, so cycle time is in nanoseconds — a very common place students make arithmetic slips. After reaching 0.4 seconds, ask: 'does this feel like a fast or slow program?' and connect it back to the response-time idea from earlier: 0.4 seconds for 200 million instructions is what real hardware achieves routinely.

## Slide 13
Worked Example 2 — Comparing Two Processors
Processor A: 2 GHz clock, CPI = 1.5. Processor B: 3 GHz clock, CPI = 2.2.
Same program, same instruction count. Which is faster?
Processor A
CCT = 1 / 2×10⁹ = 0.5 ns
CPU Time ∝ CPI × CCT
= 1.5 × 0.5 ns = 0.75 ns per instruction
Processor B
CCT = 1 / 3×10⁹ = 0.333 ns
CPU Time ∝ CPI × CCT
= 2.2 × 0.333 ns = 0.73 ns per instruction
Result: Processor B is (very slightly) faster per instruction — despite a much lower CPI advantage for A, B's higher clock rate wins out.
Notes: This example is deliberately close so students internalise the key lesson: clock rate ALONE never tells you which processor is faster — you must consider CPI together with clock rate. Let students guess before revealing the answer; many will assume 3 GHz automatically wins. Reveal that it's true here, but barely, and CPI could easily have tipped the balance the other way with slightly different numbers. This directly answers the icebreaker question about two devices with different GHz feeling different in speed.

## Slide 14
MIPS — A Tempting but Flawed Shortcut
MIPS = Millions of Instructions Per Second = Instruction Count / (CPU Time × 10⁶)
Appears simple: bigger MIPS looks like it should mean 'faster'
Problem 1:
MIPS ignores what the instructions actually do — a processor with a weak instruction set may need MORE instructions to do the same job
Problem 2:
MIPS can vary across programs on the same machine, so it is not a single fixed rating
Takeaway: always prefer actual execution time for a real workload over a single marketing number
Presidency University, Bengaluru
CSS2257
Notes: Use an analogy: judging a writer purely by 'words typed per minute' rather than the quality or correctness of the essay. A processor with a simpler, weaker instruction set might need to execute many more tiny instructions to do the same job as a smarter instruction set doing it in fewer, richer instructions — so it might report a higher MIPS while actually taking longer in real time. This is a classic exam question, so flag it clearly: MIPS can be misleading and execution time is the gold standard.

## Slide 15
Amdahl's Law — The Law of Diminishing Returns
Real programs are a mix of a part you CAN speed up (enhanceable) and a part you CANNOT (unaffected)
Amdahl's Law tells you the maximum overall speedup possible, given the fraction of time an enhancement affects
Key insight: the benefit of any enhancement is limited by the fraction of execution time it can actually affect
Speedup overall = 1 / [ (1 − Fraction enhanced) + (Fraction enhanced / Speedup enhanced) ]
Visual & Delivery Tip
Draw a pie chart: an 'improvable' slice and a 'fixed' slice, to show why gains cap out.
Presidency University, Bengaluru
CSS2257
Notes: Introduce Amdahl's Law as one of the most important laws in all of computer architecture — it applies to parallel processing, caching, virtually any optimisation. State the intuition in plain words before the formula: if only 30% of a program's time can be sped up, then even an INFINITELY fast enhancement to that 30% can only ever reduce total time by at most 30%. The other 70% is untouched and becomes the new bottleneck. This is why architects hunt for the biggest, most common bottleneck first.

## Slide 16
Amdahl's Law — Worked Example
A new floating-point unit makes floating-point operations 4× faster. FP operations account for 40% of execution time. Find the overall speedup.
1
Fraction enhanced = 0.40, Speedup of enhanced part = 4
2
Unaffected fraction = 1 − 0.40 = 0.60
3
Denominator = 0.60 + (0.40 / 4) = 0.60 + 0.10 = 0.70
4
Overall Speedup = 1 / 0.70 = 1.43×
Even a 4× local speedup on 40% of the program yields only 1.43× overall — this is Amdahl's Law in action.
Notes: Work through each step slowly, and pause on the final result. Ask students: 'we made one part 4 times faster — why isn't the whole program 4 times faster?' Reinforce: the 60% of the program untouched by the FP unit still takes exactly the same time it always did, so it caps the total benefit. This example is a very common exam-style question, so encourage students to practice plugging different fractions and speedups into this same formula.

## Slide 17
Technology Trends — Moore's Law
Gordon Moore (1965) observed that the number of transistors on a chip roughly doubles every 1–2 years
This is an empirical industry trend, not a law of physics — sustained through decades of fabrication innovation
More transistors historically enabled: more cache, more cores, wider pipelines, smarter branch prediction
Growth has slowed in recent years as transistors approach atomic-scale physical limits
Chart: Transistors per Chip (relative, log-like growth)
| 1985 | 1995 | 2005 | 2015 | 2025
Relative Transistor Count | 1 | 32 | 1024 | 16384 | 131072
Presidency University, Bengaluru
CSS2257
Notes: Show the chart and let it speak for itself first — the curve looks almost flat then suddenly explosive, which is the nature of exponential growth. Explain that this exponential transistor growth is the single biggest reason your smartphone today is vastly more capable than room-sized computers from decades ago. Mention, honestly, that the pace has been slowing recently because transistors are now only a few atoms wide, and further miniaturisation faces real physical limits — this sets up the next slide on the power wall.

## Slide 18
Technology Trends — The Power Wall
For decades, faster clock rates were the primary way to boost performance
But power consumption grows roughly with the square of voltage and linearly with frequency — pushing clock rate higher makes chips run very hot
Around the mid-2000s, industry hit the “power wall”: clock rates plateaued near 3–5 GHz because cooling could not keep up
This forced a fundamental shift in strategy: instead of one faster core, use multiple cores working together
Presidency University, Bengaluru
CSS2257
Notes: This is a pivotal, almost historical moment in computer architecture — make it feel like a turning point in the story. Before the mid-2000s, each new processor generation was mainly just a faster clock. Explain, using a simple analogy, that pushing clock rate is like pressing the accelerator on a car harder and harder: at some point the engine overheats. The industry's clever workaround was to stop trying to make one engine faster and instead add more engines — multiple cores — which is the direct motivation for parallelism, our topic in a few slides.

## Slide 19
The Processor Clock — A Closer Look
The clock is generated by a crystal oscillator on the motherboard/chip, producing a stable, repeating electrical signal
Every register in the CPU updates its value only on a clock edge (typically the rising edge)
This synchronisation is what makes a CPU a 'synchronous' digital system — all operations march in lockstep
Without a clock, results from different parts of the circuit could arrive at unpredictable times and corrupt computation
Presidency University, Bengaluru
CSS2257
Notes: Reinforce the metronome/orchestra analogy from earlier: just as a metronome keeps every musician playing in time with each other, the clock keeps every register and logic gate in the CPU updating in a coordinated, predictable rhythm. Explain that if there were no shared clock, one part of the circuit might finish a calculation microseconds before another part expects the result, causing errors — this is why virtually every general-purpose CPU today is a synchronous design built entirely around a common clock signal.

## Slide 20
Clock Rate, Cycle Time, and Overclocking
Clock Rate and Clock Cycle Time are reciprocals: Clock Rate = 1 / Clock Cycle Time
A 4 GHz processor has a cycle time of 0.25 nanoseconds; a 2 GHz processor has 0.5 nanoseconds
'Overclocking' means running the chip at a higher-than-rated frequency, shortening the cycle time
Risk: if the cycle becomes shorter than the time signals need to travel through the slowest circuit path, results become incorrect — this is why overclocking needs better cooling and voltage tuning
Presidency University, Bengaluru
CSS2257
Notes: Reinforce the reciprocal relationship with the two quick numeric examples on the slide — ask students to verify 1/(4×10^9) = 0.25 ns mentally or on paper. When explaining overclocking, connect it back to the power wall: pushing frequency higher generates more heat and, past a point, the circuit's slowest logic path (the 'critical path') simply cannot finish its work within the shortened cycle, producing wrong answers. This is why enthusiast overclockers pair higher clocks with liquid cooling and careful voltage adjustment.

## Slide 21
Why Clock Speed Alone Doesn't Decide Performance
Recall: CPU Time = IC × CPI × Clock Cycle Time — clock rate is only ONE of three multiplied factors
A high clock rate with a high CPI can lose to a lower clock rate with a low, efficient CPI (Example 2 proved this)
Different instruction sets need different instruction counts for the same task — IC is not fixed either
This is exactly why benchmark suites (e.g., SPEC) run real programs rather than trusting a single GHz figure
Presidency University, Bengaluru
CSS2257
Notes: This slide directly closes the loop on the icebreaker discussion and Worked Example 2. Ask: 'now that we know CPU time depends on three multiplied factors, can anyone explain why two phones with the same GHz might feel different?' Let a student connect it to CPI and instruction count differences between chip architectures (e.g., ARM vs x86 design philosophies, without needing deep detail). Mention SPEC benchmarks as the industry-standard, honest way to compare real performance instead of trusting a single advertised number.

## Slide 22
Introduction to Parallelism
Once clock rate hit the power wall, the only path left to more performance was doing MORE WORK PER CYCLE, not faster cycles
Parallelism = performing multiple operations at the same time instead of one after another
Three major forms studied in architecture, from finest to coarsest grain:
Instruction-Level (ILP)
Overlap multiple instructions within one core
Data-Level (DLP)
Apply one operation to many data items at once
Thread-Level (TLP)
Run independent threads on separate cores
Presidency University, Bengaluru
CSS2257
Notes: Frame this as the direct sequel to the power wall story: since we cannot keep raising clock rate, architects instead find ways to do more useful work within every single cycle. Introduce the three flavours at a high level here — we'll take one slide to unpack each in more depth next. Use a kitchen analogy: ILP is one chef doing several prep steps in overlapping order; DLP is one chef chopping ten identical vegetables with one repeated motion; TLP is hiring multiple chefs who cook different dishes independently.

## Slide 23
Instruction-Level Parallelism — Pipelining
Pipelining overlaps the execution stages of multiple instructions, like an assembly line
Classic 5 stages: Fetch → Decode → Execute → Memory Access → Write Back
While one instruction is being decoded, the next is already being fetched — no cycle is wasted waiting idle
Fetch
Decode
Execute
Memory
Write Back
Without pipelining: each instruction finishes fully before the next begins — 4 instructions take 4 × 5 = 20 cycles.
With pipelining: stages overlap — 4 instructions finish in roughly 5 + (4−1) = 8 cycles, a large speedup.
Presidency University, Bengaluru
CSS2257
Notes: Draw the classic pipeline staircase diagram on the board: instruction 1 in fetch during cycle 1, instruction 2 enters fetch during cycle 2 while instruction 1 moves to decode, and so on. This is exactly like a car wash assembly line — while one car is being rinsed, the next is already being soaped, and a third is being dried, all simultaneously at different stations. Mention briefly that hazards (data dependencies, branches) can stall the pipeline in practice, but the ideal case shown here captures the core idea perfectly.

## Slide 24
Data-Level Parallelism — SIMD
SIMD = Single Instruction, Multiple Data — one instruction operates on several data elements simultaneously
Common in graphics processing, image filters, and scientific computing where the same operation repeats over large arrays
Modern CPUs include SIMD extensions (e.g., wide vector units); GPUs take this idea to an extreme with thousands of parallel lanes
ADD instruction, applied to 4 pairs at once:
2
+
3
=
5
5
+
4
=
9
1
+
6
=
7
8
+
2
=
10
All four additions happen in the same clock cycle — not one after another.
Presidency University, Bengaluru
CSS2257
Notes: Point to the four addition rows and stress the word 'simultaneously' — in a scalar processor, these four additions would need four separate instructions and four separate cycles; in SIMD, one instruction and effectively one cycle handles all four. Give a relatable example: applying a brightness filter to a photo means adding the same value to every pixel — SIMD is exactly suited to this kind of repetitive, uniform operation, which is why GPUs (built almost entirely around this idea) excel at graphics and, more recently, AI workloads.

## Slide 25
Thread-Level Parallelism — Multicore
TLP runs separate, largely independent threads or processes on separate processor cores at the same time
This is the direct architectural response to the power wall: instead of one faster core, place several moderately-fast cores on one chip
Operating systems schedule different applications — or different parts of the same application — onto different cores
Speedup from adding cores is governed by Amdahl's Law: the serial (non-parallelisable) portion of a program limits the benefit
Quad-Core Chip
Core 1
Thread 1
Core 2
Thread 2
Core 3
Thread 3
Core 4
Thread 4
Presidency University, Bengaluru
CSS2257
Notes: Show the quad-core diagram and describe a concrete scenario: while you browse the web on one core, a music app decodes audio on a second core, a background update runs on a third, and antivirus scans on a fourth — all genuinely simultaneous, not just fast switching. Circle back to Amdahl's Law explicitly here: adding more cores only helps the portion of work that can actually be split among them; a program that is mostly one long sequential chain of dependent steps won't benefit much no matter how many cores you add.

## Slide 26
Real-World Example — A Smartphone's Chip
A modern smartphone System-on-Chip (SoC) uses all three forms of parallelism at once
ILP:
each CPU core pipelines and overlaps its own instructions internally
DLP:
the GPU applies SIMD-style operations across millions of pixels for the display
TLP:
big/little core clusters run different apps and background tasks on separate cores simultaneously, balancing performance and battery life
Presidency University, Bengaluru
CSS2257
Notes: Bring the whole lecture together with a device every student is holding right now. Ask them to picture what happens when they scroll a social media feed: the CPU cores overlap instruction execution internally (ILP), the GPU processes every pixel of the screen in parallel (DLP), and separate cores simultaneously handle the app, background network sync, and audio (TLP) — all while a power-management system juggles clock rate against battery life, tying directly back to the power wall discussion.

## Slide 27
Common Misconceptions & Pitfalls
“Higher GHz always means faster”
False — CPI and instruction count matter just as much (see Example 2)
“More cores always means proportionally faster”
False — Amdahl's Law caps the benefit based on the serial fraction
“MIPS is a fair way to compare processors”
Misleading — it ignores instruction quality and varies by program
“Overclocking is free performance”
Risky — can violate timing margins and cause incorrect results
Presidency University, Bengaluru
CSS2257
Notes: Go through these quickly as a rapid-fire myth-busting round — read the misconception, pause, ask 'true or false?', then reveal the correction. Each one maps directly back to something already taught in this lecture, so use this slide as a review checkpoint as much as a myths list: it naturally tests whether the CPU time equation, Amdahl's Law, MIPS limitations, and the clock/timing relationship have actually landed with students before the quiz.

## Slide 28
Quick Check — Think, Pair, Share
A processor's clock rate is doubled, but its CPI also doubles for the same program. What happens to CPU execution time?
Take 60 seconds to work this out individually
Turn to your neighbour and compare your reasoning for 60 seconds
We'll take 2–3 volunteers to share their answer with the class
Hint
Cycle time is halved AND CPI is doubled — substitute both changes into CPU Time = IC × CPI × CCT and see what cancels.
Presidency University, Bengaluru
CSS2257
Notes: Run this as a genuine think-pair-share: give a full 60 seconds of silent individual thinking time first, resist the urge to rush it. Then let pairs discuss for 60 seconds. Cold-call or ask for volunteers, and guide them to see that doubling clock rate halves cycle time, but doubling CPI cancels that benefit exactly — so CPU time stays unchanged. Use this as a natural bridge into the summary: it's a perfect, concrete illustration of why all three factors in the performance equation must be considered together.

## Slide 29
Summary of Key Points
Performance means different things: response time for one user, throughput for a whole system
CPU Time = Instruction Count × CPI × Clock Cycle Time — the master equation of this lecture
Clock Rate and Clock Cycle Time are reciprocals; the clock synchronises every part of the CPU
MIPS and raw GHz are misleading shortcuts — always reason with the full performance equation
Amdahl's Law shows any enhancement's benefit is capped by the fraction of time it affects
The power wall pushed the industry from 'faster clocks' to 'more parallelism': ILP, DLP, and TLP
Presidency University, Bengaluru
CSS2257
Notes: Recap each bullet briefly in one sentence, connecting it back to the specific slide or example where it was introduced — this repetition genuinely helps retention. Tell students that if they can explain each of these six bullets in their own words to a friend, they have mastered today's material. Let them know the quiz that follows directly tests these exact six ideas, so this is their final review moment before it begins.

## Slide 30
Quiz — CSS2257
Q1 (T/F): Response time and throughput always improve together.
Q2 (MCQ): CPU Time equals IC × CPI × ____. (a) MIPS (b) Clock Cycle Time (c) Clock Rate
Q3 (Short): Define CPI in one sentence.
Q4 (Calc): Clock rate = 2.5 GHz. What is the clock cycle time?
Q5 (T/F): A processor with higher MIPS is always the faster processor.
Q6 (Short): State Amdahl's Law's key limiting idea in your own words.
Q7 (MCQ): SIMD is an example of — (a) ILP (b) DLP (c) TLP
Q8 (Short): Why did the industry hit the 'power wall'?
Presidency University, Bengaluru
CSS2257
Notes: Give students 4 to 5 minutes to attempt all eight questions individually, on paper or notebook — make clear this is a self-check for understanding, not a graded assessment, so they should answer honestly rather than guess to please you. Encourage them to attempt every question even if unsure, since the goal is to surface what needs revisiting. Walk around the room if possible to see how confidently they're answering, which helps you gauge pacing for the reveal that follows.

## Slide 31
Quiz Answers — CSS2257
A1: False — an enhancement can raise throughput while response time for an individual task stays the same or worsens.
A2: (b) Clock Cycle Time — CPU Time = IC × CPI × Clock Cycle Time.
A3: CPI is the average number of clock cycles used per instruction for a given program on a given machine.
A4: Clock Cycle Time = 1 / 2.5×10⁹ = 0.4 nanoseconds.
A5: False — MIPS ignores instruction quality and can vary across programs (see Slide 14).
A6: The overall speedup from any enhancement is limited by the fraction of execution time it can affect — the untouched portion becomes the bottleneck.
A7: (b) DLP — SIMD applies one instruction to many data items simultaneously.
A8: Rising clock rates caused power/heat to grow faster than performance gain, so cooling could no longer keep pace — forcing a shift toward multicore parallelism.
Presidency University, Bengaluru
CSS2257
Notes: Go through each answer in order, briefly restating the reasoning rather than just reading the answer — e.g., for A4 actually show the division 1/(2.5×10^9) on the board once more. Ask for a show of hands on each question to see how many got it right; this gives you an informal read on which concepts need a quick revisit next class. Close by telling students which points were most commonly missed, and encourage them to note those down for their own revision before the next session.

## Slide 32
Further Reading & What's Next
Further Reading
Hennessy & Patterson, Computer Organization and Design — Chapter on Performance
Any standard COA textbook chapter covering the CPU performance equation and Amdahl's Law
Assignment Idea
Pick two real processors (from spec sheets online) and estimate which performs better on a hypothetical workload, showing your working
What's Next
Next class: Instruction Set Architecture and how instructions are actually encoded and executed
Presidency University, Bengaluru
CSS2257
Notes: Close the session on a forward-looking note. Briefly describe the assignment idea as an optional but valuable exercise: finding two real processor spec sheets online and reasoning through which is likely faster for a given workload using today's tools, not just marketing numbers. Preview next class briefly — instruction set architecture — and tell students it will build directly on today's IC and CPI concepts. Thank the class and open the floor for any final questions before wrapping up.