## Slide 1
IF
ID
EX
MEM
WB
CSS2257 • Computer Organization and Architecture
Basic Performance Equation
Stalls & Penalties • Pipeline Depth • Clock Rate • Performance Metrics
CPU Time = IC × CPI × Clock Cycle Time
University
Presidency University, Bengaluru
School
School of Artificial Intelligence and Advanced Computing
Department
Department of AI & Robotics
Faculty
Manoj Sagar
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
Notes: Welcome everyone. Today's session is part of our ongoing journey through Computer Organization and Architecture (CSS2257), and we are going to answer a question every computer engineer eventually asks: "how fast is this processor, really?" We'll build up the Basic Performance Equation from scratch, see how pipeline stalls and penalties eat into that performance, look at why the number of pipeline stages is a double-edged sword, and finally learn how to measure performance honestly using clock speed and instruction execution rate. By the end of this hour you'll be able to calculate CPU execution time for a real program and explain why "more GHz" or "more MIPS" doesn't automatically mean "faster computer." Let's get started.

## Slide 2
COURSE INFORMATION
Where This Lecture Fits
SUBJECT
Computer Organization and Architecture (CSS2257)
SCHOOL
School of Artificial Intelligence and Advanced Computing
DEPARTMENT
Department of AI & Robotics
FACULTY
Manoj Sagar
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
1
Notes: Quick orientation slide -- this lecture is delivered under the Computer Organization and Architecture course, code CSS2257, offered by the Department of AI & Robotics within the School of Artificial Intelligence and Advanced Computing at Presidency University, Bengaluru. This sits right after our earlier sessions on processor clock and basic operational concepts, so today we go one level deeper into how we actually quantify performance.

## Slide 3
SESSION ROADMAP
Learning Objectives
State and apply the Basic Performance Equation to compute CPU execution time.
Explain how pipeline stalls and penalties inflate the effective CPI.
Analyze the trade-off between the number of pipeline stages and clock rate.
Differentiate clock rate from real instruction throughput.
Compute and critique performance using clock speed and instruction execution rate (MIPS).
Identify common misconceptions when comparing processor performance.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
2
Notes: Here is where we are headed this hour. By the end you should be able to sit down with a program's instruction count, its CPI, and a clock rate, and confidently compute -- and interpret -- how long that program actually takes to run. We'll also arm you against two of the most common traps in this course and in industry marketing: assuming higher clock speed means a faster machine, and assuming a bigger MIPS number means a better processor. Keep these six objectives in the back of your mind as we go.

## Slide 4
WARM-UP
Icebreaker: Before We Begin
Q1
When you shop for a laptop or phone, what number do you look at first -- GHz, RAM, or something else?
Q2
Have you ever felt a "fast" processor still feel slow while multitasking? Why do you think that happens?
Q3
If Processor A runs at 4 GHz and Processor B at 2 GHz, is A definitely faster? Quick show of hands.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
3
Notes: Let's warm up before diving into formulas. Pose these one at a time -- take quick show-of-hands or a couple of verbal answers, don't let any single question eat more than a minute. The goal is to surface their existing (often marketing-driven) intuitions about "fast processors" so we can gently correct them over the next 45 minutes. The third question is the real hook -- most students will instinctively say "yes, A is faster," and you can tell them: "hold that thought, we'll revisit this exact question in 10 minutes." Use their answers to transition into why this topic matters.

## Slide 5
MOTIVATION
Why This Topic Matters
Every performance claim you see -- "30% faster," "2x GHz," "10,000 MIPS" -- has to be interpreted through a formula, not taken at face value.
Chip designers spend billions of dollars deciding pipeline depth: too shallow wastes clock speed potential, too deep multiplies stall penalties.
Compiler and OS engineers tune code specifically to reduce CPI -- fewer branch mispredictions, fewer memory stalls -- because CPI, not just clock rate, drives real-world speed.
Interview and exam questions in computer architecture almost always come back to this one equation, in disguise.
Real-world stakes
A single extra pipeline stall per instruction, at 3 GHz, over a billion instructions, costs real seconds users can feel.
Data centers pay for every wasted cycle -- in electricity and in cooling.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
4
Notes: So why should you, as future engineers, care about a formula? Because this equation is the referee for every performance claim you'll ever read. When NVIDIA or Intel or Apple announces a new chip, marketing gives you one or two numbers -- but the real story is always Instruction Count, CPI, and Clock Cycle Time interacting. Understanding this equation is what separates someone who can read a spec sheet from someone who can actually evaluate a system. It's also foundational -- almost every later topic in this course, from caches to superscalar execution, is really just another way of shrinking one of these three terms.

## Slide 6
FOUNDATIONS
Recap: What Is CPU Time?
CPU Time (or CPU Execution Time) is the total time the processor spends actively executing a given program.
It excludes time waiting on I/O, waiting for the OS scheduler, or sitting idle -- it is purely the processor’s own working time.
It is measured in seconds, and it is the single most honest measure of "how long did this program take to run on this chip."
Everything we do today is really about predicting and reducing this one number.
CPU Time
The wall-clock seconds the CPU itself spends executing your program’s instructions -- start to finish.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
5
Notes: Quick recap from our earlier session on basic operational concepts: CPU time is not the same as "elapsed time" you'd see on a stopwatch while a program runs -- that also includes disk waits, network waits, other processes taking turns. CPU time isolates just the processor's own effort. This distinction matters because our formula today predicts CPU time specifically, and it's the number architects actually optimize.

## Slide 7
KEY TERM 1 OF 3
Instruction Count (IC)
The total number of machine instructions actually executed while running the program -- not the number of lines in the source code.
Depends heavily on the algorithm and the instruction set architecture (ISA): a loop that runs 1,000 times contributes 1,000× its body’s instructions.
A single high-level statement can expand into many machine instructions, and that expansion factor changes with compiler optimization.
Symbol: IC. Typical scale: millions to billions of instructions for real programs.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
6
Notes: First of our three building blocks: Instruction Count. A common student mistake is confusing "lines of code" with instruction count -- they are not the same. A single C statement like "a = b + c * d" might compile into three or four machine instructions. And a loop that iterates a thousand times executes its body a thousand times over, even though it's written once in the source. IC captures dynamic behavior, not static code size.

## Slide 8
KEY TERM 2 OF 3
CPI — Cycles Per Instruction
The average number of clock cycles it takes to execute one instruction, averaged across the whole program.
In an ideal, hazard-free pipeline, CPI approaches 1 -- one instruction finishes roughly every cycle.
Real CPI is almost always higher than ideal, because of pipeline stalls, cache misses, and branch mispredictions -- the exact topic of our next section.
Symbol: CPI. Formula: CPI = Total Clock Cycles ÷ Instruction Count.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
7
Notes: Second building block: CPI, cycles per instruction. Think of it as "how many turns of the clock does the average instruction cost me." A perfectly pipelined, hazard-free processor would love a CPI of exactly 1.0 -- meaning every single clock tick retires one instruction. But real programs on real hardware almost never hit that, because of the stalls we're about to discuss. This is the term most directly under the compiler and hardware designer's control.

## Slide 9
KEY TERM 3 OF 3
Clock Cycle Time & Clock Rate
Clock Cycle Time (T_clock) is the duration of one clock tick, in seconds (commonly nanoseconds).
Clock Rate is its reciprocal: Clock Rate = 1 ÷ Clock Cycle Time, measured in Hertz (GHz today).
A 3 GHz processor has a clock cycle time of about 0.33 nanoseconds -- three billion ticks every second.
Faster clock rate shortens each tick, but it does not by itself change how many ticks an instruction needs -- that is CPI’s job.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
8
Notes: Our third and final building block: clock rate and clock cycle time -- two sides of the same coin, reciprocals of each other. This is the number that appears on every box and spec sheet -- "3.5 GHz," "4.2 GHz." It genuinely matters, but notice the last bullet: clock rate only tells you how long each tick is. It says nothing about how many ticks each instruction needs. That's exactly the trap our icebreaker Question 3 was setting up -- and we're about to formalize why "higher GHz" alone can mislead you.

## Slide 10
THE CORE FORMULA
The Basic Performance Equation
CPU Time = IC × CPI × Tclock
IC
Instructions executed (count)
CPI
Average cycles per instruction
Clock Time
Seconds per clock cycle
Three independent levers. Move any one, and CPU time moves with it.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
9
Notes: Here it is -- the single most important equation in this entire course: CPU Time equals Instruction Count times CPI times Clock Cycle Time. Say it out loud with the class once. Every processor performance question you will ever face reduces to changing one of these three variables while (usually) holding the others fixed, or trading one off against another. Compilers attack IC. Pipeline and hazard design attacks CPI. Process technology and pipeline depth attack clock cycle time. Today we go deep on the second and third terms.

## Slide 11
FROM CYCLES TO SECONDS
Deriving the Equation
1
Total Clock Cycles
The processor spends some number of clock ticks executing the whole program.
2
Cycles per Instruction
On average, each instruction consumes CPI cycles, so Total Cycles = IC × CPI.
3
Seconds per Cycle
Each cycle lasts T_clock seconds, so we convert cycles to time by multiplying.
4
CPU Time
CPU Time = (IC × CPI) × T_clock — our Basic Performance Equation.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
10
Notes: Let's not just memorize the formula -- let's derive it, so it sticks. Step one: the program consumes some total number of clock cycles. Step two: since CPI is the average cost per instruction, total cycles is just Instruction Count times CPI. Step three: each of those cycles takes T-clock seconds, a fixed hardware property. Multiply cycles by seconds-per-cycle and you get seconds -- actual wall-clock CPU time. This derivation is worth being able to reproduce from memory in an exam.

## Slide 12
TRADE-OFFS
The Three Performance Levers
Reduce IC
COMPILER / ALGORITHM DESIGNER
Better algorithms, compiler optimizations, richer instructions that do more per instruction.
Reduce CPI
PIPELINE / MICROARCHITECT
Fewer stalls, better branch prediction, hazard forwarding, deeper pipelining.
Reduce Clock Cycle Time
FABRICATION / CIRCUIT DESIGNER
Smaller transistors, better process node, shorter critical path per stage.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
11
Notes: Since CPU time is a product of three terms, three different specialists spend their careers attacking three different levers. Compiler writers and algorithm designers shrink Instruction Count. Microarchitects -- the pipeline designers -- shrink CPI by removing stalls, which is where we're headed next. And chip fabrication engineers shrink clock cycle time by cramming more, smaller, faster transistors onto silicon. Crucially: pulling one lever can push another the wrong way -- that tension is exactly what we explore with pipeline depth in a few slides.

## Slide 13
FROM IDEAL TO REAL CPI
What Are Pipeline Stalls?
A stall (or "bubble") is a clock cycle in which the pipeline cannot make forward progress on the next instruction.
The processor effectively "wastes" that cycle -- no useful instruction completes during it.
Stalls happen because one instruction is not yet ready to be fed into the pipeline -- data it needs, or the next instruction it needs, is not available yet.
Every stall cycle directly raises the effective CPI above its ideal value of 1.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
12
Notes: We said real CPI is almost always above the ideal of 1. The reason is stalls -- sometimes called pipeline bubbles. Picture the pipeline as an assembly line: if station three has to wait because the part from station two isn't ready, the whole line pauses for a beat. That paused beat is a stall cycle -- no instruction finishes during it, but the clock still ticks. Multiply that wasted cycle across millions of instructions, and it becomes a very real performance cost.

## Slide 14
THREE CULPRITS
Types of Pipeline Stalls
Structural Hazard
Two instructions need the same hardware resource (e.g., one memory port) at the same time.
Data Hazard
An instruction needs a result that a previous, still-in-flight instruction hasn’t produced yet.
Control Hazard
A branch instruction hasn’t been resolved yet, so the pipeline doesn’t know which instruction to fetch next.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
13
Notes: Three named culprits behind stalls. Structural hazards: two instructions literally fighting over the same physical resource, like a single memory port. Data hazards: an instruction needs an operand that an earlier instruction, still mid-flight in the pipeline, hasn't produced yet -- think "add uses a register that a load two instructions earlier hasn't finished loading." Control hazards: the classic branch problem -- the pipeline doesn't yet know if a branch will be taken, so it doesn't know what to fetch next. We'll zoom into control hazards specifically in a couple of slides, since they tend to be the costliest.

## Slide 15
QUANTIFYING THE DAMAGE
Effect of Stalls and Penalties on CPI
CPI = CPI_ideal + Stall Cycles per Instruction
CPI_ideal is what CPI would be with zero hazards -- typically 1.0 for a simple scalar pipeline.
Stall Cycles per Instruction = (fraction of instructions that stall) × (penalty cycles per stall).
This is exactly the same shape as Amdahl’s-style reasoning: frequency of an event × cost of that event.
Reducing either the frequency of stalls (better prediction, better scheduling) or the penalty per stall (shorter pipeline recovery) directly lowers CPI -- and therefore CPU time.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
14
Notes: Now we quantify it. The real, effective CPI is the ideal CPI plus however many extra stall cycles each instruction costs on average. And that stall term itself breaks down further: how often does the bad event happen, times how expensive it is when it does. This "frequency times penalty" pattern is going to reappear constantly in this course -- cache misses, TLB misses, branch mispredictions -- they're all the same mathematical shape. Master this one formula and half of computer architecture performance analysis becomes pattern matching.

## Slide 16
CONTROL HAZARDS IN DETAIL
Branch Penalty — A Closer Look
When the pipeline fetches a branch, it doesn’t yet know if the branch will be taken -- but it must fetch something next.
If it guesses wrong (or simply waits), the instructions already fetched must be discarded -- a "pipeline flush."
Every flushed instruction costs one stall cycle -- deeper pipelines flush more instructions per misprediction.
Branch penalty (cycles) × branch misprediction rate becomes a direct addition to CPI, exactly as in the formula on the previous slide.
Worked mini-example
20% of instructions are branches
30% of those are mispredicted
Misprediction penalty = 3 cycles
CPI added = 0.20 × 0.30 × 3 = 0.18 cycles/instr
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
15
Notes: Branch penalties deserve special attention because they're usually the single biggest contributor to real-world CPI inflation. When the fetch stage hits a branch, it has to guess what comes next -- taken or not taken -- and keep the pipeline full while the branch condition is still being computed. Guess wrong, and everything fetched behind that guess is worthless and must be flushed, costing several cycles. Walk through the worked example on the right with the class: multiply the branch frequency, by the misprediction rate, by the penalty, and you get the CPI contribution -- here, 0.18 extra cycles per instruction, which sounds small until you remember it applies to every single instruction in the program.

## Slide 17
PIPELINE DEPTH
What Are Pipeline Stages?
IF
Instruction Fetch
ID
Instr. Decode / Reg. Read
EX
Execute / ALU
MEM
Memory Access
WB
Write Back
A pipeline stage is one step of instruction processing that can run in parallel, in the same cycle, with other instructions’ other stages.
The classic five-stage RISC pipeline shown above lets up to five different instructions be "in flight" simultaneously, one per stage.
Each stage’s work must fit inside one clock cycle -- the slowest stage sets the clock cycle time for the whole pipeline.
More stages = each stage does less work = each stage can be shorter = the clock can potentially run faster.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
16
Notes: Let's connect stalls back to pipeline structure itself. A pipeline stage is one slice of the instruction's journey -- fetch, decode, execute, memory access, write-back, in the classic five-stage design. The trick of pipelining is that while instruction 5 is being fetched, instruction 4 can be decoding, instruction 3 executing, and so on -- five instructions genuinely in flight at once. The critical insight for the next slide: the clock cycle time is dictated by whichever single stage takes the longest. If you split a slow stage into two shorter ones, you can run the clock faster.

## Slide 18
THE CORE TRADE-OFF
Number of Pipeline Stages vs. Clock Rate
Fewer, Deeper Stages
Each stage does more work → takes longer → clock cycle time is longer → clock rate is lower.
Fewer pipeline boundaries → fewer hazards → CPI stays closer to ideal.
Simpler control logic, easier to design and verify.
More, Shallower Stages
Each stage does less work → takes less time → clock cycle time is shorter → clock rate is higher.
More pipeline boundaries → more hazards possible → branch and data stalls get more expensive (bigger flush penalty).
CPI tends to rise even as clock rate rises -- the two effects fight each other.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
17
Notes: This is the heart of today's trade-off. Split the pipeline into more stages, and each individual stage becomes simpler and faster -- so the clock cycle time shrinks and the clock rate you can advertise goes up. Sounds great, right? But remember our CPI formula: more stages generally means a longer path for data to travel between where it's produced and where it's needed, and a bigger flush penalty when a branch is mispredicted, because more instructions are "in flight" and have to be discarded. So CPI creeps upward even as clock rate climbs. Which effect wins? That depends entirely on the workload -- which is exactly why chip designers don't just keep adding stages forever.

## Slide 19
WEIGHING THE TRADE-OFF
Deeper Pipelines: Benefit vs. Cost
Factor
Shallow Pipeline (few stages)
Deep Pipeline (many stages)
Clock rate
Lower
Higher
CPI (ideal)
Close to 1
Still close to 1
Branch mispredict penalty
Small
Large
Data hazard exposure
Lower
Higher
Design & verification effort
Lower
Higher
Net CPU Time
Depends on workload
Depends on workload
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
18
Notes: Let's lay the trade-off out as a table, since students often want a clean reference for revision. Walk down each row: shallow pipelines keep CPI low and design simple but cap your clock rate; deep pipelines unlock higher clock rates but raise your branch and data hazard exposure, and are much harder to verify correctly. The last row is deliberately unresolved -- "depends on workload" -- because that is the honest, examinable answer. A branch-heavy program (lots of if-statements) suffers more from deep pipelines than a branch-light, arithmetic-heavy program does.

## Slide 20
REAL-WORLD EXAMPLE
Pipeline Depths in Real Processors
Classic RISC (MIPS)
5 stages
Textbook baseline: IF-ID-EX-MEM-WB.
ARM Cortex-A53
~8 stages
In-order, mobile-class -- balances battery life and speed.
Pentium 4 (Prescott)
~31 stages
Chased very high clock rates; paid a heavy branch-mispredict penalty.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
19
Notes: Approximate, illustrative figures, but the story is real and well documented in architecture history. The textbook 5-stage RISC pipeline is our teaching baseline. ARM's Cortex-A53, used in countless phones, sits around eight stages -- a deliberate middle ground because mobile chips care about battery life as much as raw speed. Intel's Pentium 4 "Prescott" generation famously pushed past thirty pipeline stages chasing clock-rate bragging rights -- and became the textbook cautionary tale, because branch mispredictions became so costly that real-world performance often disappointed despite the huge GHz numbers. This is precisely why the industry pulled back toward shallower, smarter pipelines afterward.

## Slide 21
WORKED EXAMPLE 1
Basic CPU Time — Problem Statement
A program executes 50 million (50 × 10⁶) instructions.
The processor has a clock rate of 2 GHz (2 × 10⁹ Hz).
The average CPI for this program on this processor is 1.5.
Find: the total CPU execution time, in seconds.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
20
Notes: Time to put the equation to work. Read the problem aloud and let students jot down the three given values before you move to the next slide: IC = 50 million, clock rate = 2 GHz, CPI = 1.5. Ask them: "which formula do we reach for?" -- give them thirty seconds to attempt it themselves on paper before revealing the step-by-step solution.

## Slide 22
WORKED EXAMPLE 1
Step-by-Step Solution
Step 1 — Write the formula
CPU Time = IC × CPI × T_clock = IC × CPI ÷ Clock Rate
Step 2 — Substitute values
IC = 50 × 10⁶, CPI = 1.5, Clock Rate = 2 × 10⁹ Hz
Step 3 — Compute total cycles
Total Cycles = IC × CPI = 50×10⁶ × 1.5 = 75 × 10⁶ cycles
Step 4 — Convert cycles to time
CPU Time = 75×10⁶ ÷ 2×10⁹
Step 5 — Simplify
= 37.5 × 10⁻³ seconds
Final Answer
CPU Time = 37.5 milliseconds
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
21
Notes: Walk through this out loud, step by step, don't skip the unit conversion. First restate the formula, noting that dividing by clock rate is identical to multiplying by clock cycle time -- both are valid and students will see both forms in textbooks. Substitute the given numbers. Compute total cycles first: 75 million cycles. Then divide by the clock rate to get seconds: 37.5 thousandths of a second, or 37.5 milliseconds. Pause here and ask: "does that feel fast or slow for 50 million instructions?" It's a good moment to build intuition for realistic magnitudes.

## Slide 23
WORKED EXAMPLE 2
Effect of Stalls — Problem Statement
A processor has an ideal CPI (no hazards) of 1.0, running at 1 GHz.
The program has 10 million (10 × 10⁶) instructions.
20% of instructions are branches, and each branch that stalls the pipeline costs 2 extra cycles.
Find: (a) actual CPI, and (b) how much CPU time is lost to stalls, vs. the ideal case.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
22
Notes: Now we bring stalls into the same equation, tying together everything from the middle of the lecture. Same instruction count magnitude as before but a slower, 1 GHz clock, so the numbers stay easy to follow. Emphasize: this is exactly the CPI = CPI-ideal + stall cycles per instruction formula from slide 15, now combined with the Basic Performance Equation from slide 10. Give students a minute to identify which numbers plug into which part of the formula before revealing the solution.

## Slide 24
WORKED EXAMPLE 2
Step-by-Step Solution
Step 1 — Extra CPI from stalls
Stall CPI = (branch freq.) × (penalty) = 0.20 × 2 = 0.4
Step 2 — Actual CPI
CPI = CPI_ideal + Stall CPI = 1.0 + 0.4 = 1.4
Step 3 — CPU Time (actual)
= IC × CPI ÷ Clock Rate = 10×10⁶ × 1.4 ÷ 1×10⁹ = 14 ms
Step 4 — CPU Time (ideal, no stalls)
= 10×10⁶ × 1.0 ÷ 1×10⁹ = 10 ms
Step 5 — Time lost to stalls
14 ms − 10 ms = 4 ms lost
Final Answer
CPI = 1.4 | 40% more CPU time than the hazard-free ideal
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
23
Notes: This is the payoff slide -- it makes the abstract CPI formula feel concrete. First we compute the CPI penalty purely from branches: 0.4 extra cycles per instruction, pushing actual CPI to 1.4. Then we run the full Basic Performance Equation twice -- once with the real, stall-inflated CPI, and once with the ideal CPI of 1.0 -- and compare. The program takes 14 milliseconds in reality versus 10 milliseconds in a hazard-free fantasy world -- a full 40% slower, purely because of branch stalls. Emphasize: this is the exact mechanism by which "more pipeline stages, badly handled" translates into disappointing real-world speed, tying straight back to the Pentium 4 example.

## Slide 25
MEASURING PERFORMANCE
Performance Measurement: Clock Speed
Clock speed (clock rate) is the easiest number to measure and market -- it is simply how many cycles occur per second.
It is a genuinely important input to performance -- doubling clock rate, with everything else fixed, halves CPU time.
But clock speed alone tells you nothing about CPI or Instruction Count -- and both of those can vary enormously between chip designs.
Comparing two different processor families purely by GHz is comparing one-third of the equation and ignoring the other two-thirds.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
24
Notes: Let's return to our icebreaker question: is a 4 GHz processor definitely faster than a 2 GHz one? Clock speed is real, it's measurable, and it's marketable -- which is exactly why it dominates advertising. But we've just spent the whole lecture proving that CPU time depends equally on CPI and instruction count. A 2 GHz chip with CPI of 1.0 can easily outperform a 4 GHz chip with CPI of 2.5. Clock speed is necessary information, but never sufficient information, for a performance comparison.

## Slide 26
THE TRAP
Why Clock Speed Alone Misleads Us
Processor A: 4 GHz
CPI = 2.5 (deep pipeline, many stalls)
IC = 100 million instructions
CPU Time = 100×10⁶ × 2.5 ÷ 4×10⁹ = 62.5 ms
Processor B: 2 GHz
CPI = 1.0 (shallow, hazard-free pipeline)
IC = 100 million instructions
CPU Time = 100×10⁶ × 1.0 ÷ 2×10⁹ = 50 ms
The 2 GHz processor finishes faster. This is the "Megahertz Myth."
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
25
Notes: Direct answer to our icebreaker, with real numbers side by side. Processor A boasts double the clock speed but has a bloated CPI of 2.5 from an overly deep, stall-prone pipeline -- 62.5 milliseconds. Processor B, at half the clock speed but a clean CPI of 1.0, finishes in 50 milliseconds -- genuinely faster despite the lower GHz. This exact scenario played out historically: AMD famously beat higher-clocked Pentium 4 chips in real workloads for precisely this reason, which is why the industry nicknamed this the "Megahertz Myth." Make sure students can reproduce this comparison calculation themselves.

## Slide 27
AN ALTERNATIVE METRIC
Instruction Execution Rate: MIPS
MIPS = Instruction Count ÷ (CPU Time × 10⁶) = Clock Rate ÷ (CPI × 10⁶)
MIPS stands for Million Instructions Per Second -- a direct measure of instruction throughput.
It rises when clock rate rises, and falls when CPI rises -- so, unlike clock speed alone, it does account for CPI.
Higher MIPS looks intuitively like "more work done per second," which is why it became popular as a marketing number in the 1980s-90s.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
26
Notes: Since clock speed alone was clearly insufficient, the industry reached for a metric that folds in CPI too: MIPS, Million Instructions Per Second. Notice the formula: it's literally Clock Rate divided by CPI, scaled to millions -- so a processor with high clock rate AND low CPI gets a high MIPS score, which intuitively feels like the right answer. It seems like exactly the fix we need. But -- and this is the twist for the next slide -- MIPS has its own serious blind spot.

## Slide 28
THE CATCH
Pitfalls of Using MIPS
MIPS counts instructions, but different instruction sets do very different amounts of "work" per instruction -- a CISC instruction may do what three RISC instructions do.
A processor could "cheat" a MIPS benchmark by using more, simpler instructions -- inflating MIPS while doing the same real work.
MIPS ignores the program’s actual task -- it says nothing about which program was run, or whether that program matters to the user.
Comparing MIPS across different instruction set architectures (ISAs) is comparing incompatible units -- it is often called "Meaningless Indicator of Performance."
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
27
Notes: Here's the catch, and it's a classic exam trap: MIPS treats every instruction as equal, but instructions are not equal in the work they accomplish. One complex CISC instruction might replace three or four simpler RISC instructions doing the same job -- so a RISC chip executing more, smaller instructions per second can post a higher MIPS number while doing identical real work, or even less. This is exactly why some architects joke that MIPS really stands for "Meaningless Indicator of Performance" when used to compare across different instruction set architectures. The only fair MIPS comparison is the same program, same ISA, different implementations.

## Slide 29
THE HONEST ANSWER
Better Metrics: Execution Time & Benchmarks
Actual Execution Time
The only metric that can never be gamed -- seconds to finish a real, agreed-upon task, on real hardware.
Standard Benchmark Suites (e.g., SPEC)
A fixed, representative bundle of real programs, run identically on every candidate processor, so comparisons are apples-to-apples.
Workload-Specific Benchmarking
For any real decision, measure performance on the actual software you intend to run -- generic scores are only a starting hint.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
28
Notes: So what should you actually trust? Execution time on a real task is the gold standard -- it can't be gamed the way clock speed or MIPS can, because it directly answers "how long did I wait." Since running every possible program on every possible chip isn't practical, the industry agreed on standardized benchmark suites like SPEC, which bundle a representative mix of real-world programs and report execution time or a derived score. And for your own engineering decisions -- picking a chip for a product -- always benchmark the software you actually care about, because generic scores are, at best, a starting hint.

## Slide 30
WATCH OUT
Common Misconceptions & Pitfalls
Higher clock rate always means faster.
False — only true if CPI and IC are held equal.
Higher MIPS always means better performance.
False — MIPS ignores work-per-instruction and program identity.
More pipeline stages always improves performance.
False — stall/flush penalties grow with depth.
CPI of 1 is the best any pipeline can do.
Roughly true for a simple scalar pipeline — superscalar designs can beat it.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
29
Notes: A quick myth-busting round-up, useful right before revision. Go through each claim and ask the class "true or false?" before revealing the answer on the right. The last one is deliberately more nuanced than the others -- a reminder that this course will later introduce superscalar and out-of-order designs that can push CPI below 1 by completing more than one instruction per cycle, so "CPI = 1 is the ceiling" is only true for the simple, single-issue pipeline we've studied today.

## Slide 31
CHECK YOUR UNDERSTANDING
Quick Check / Mini Activity
A processor runs at 2.5 GHz with an ideal CPI of 1.0. Adding a new feature raises the clock rate to 3 GHz but also raises CPI to 1.3 (more stalls). For a fixed 20-million-instruction program, is the new design faster or slower?
Work in pairs for 2 minutes -- compute CPU Time for both designs.
Old: CPU Time = 20×10⁶ × 1.0 ÷ 2.5×10⁹ = 8 ms
New: CPU Time = 20×10⁶ × 1.3 ÷ 3×10⁹ ≈ 8.67 ms
Answer: the "upgraded," higher-clocked design is actually slower.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
30
Notes: Time for a hands-on check before we summarize. Give students two minutes in pairs to work this through on paper -- don't reveal the numbers on the bottom half immediately, cover them or advance the animation if you're presenting live. It's deliberately built to feel like an "upgrade" (higher clock rate) that is secretly a regression once CPI is accounted for -- reinforcing the Megahertz Myth lesson from earlier with a fresh number. After two minutes, cold-call a pair or two, then reveal the worked steps.

## Slide 32
WRAP-UP
Summary of Key Points
CPU Time = IC × CPI × T_clock -- the equation behind every performance claim.
CPI = CPI_ideal + stall cycles per instruction -- stalls come from structural, data, and control hazards.
Pipeline depth trades clock rate against stall/flush penalty -- there is no free lunch.
Clock speed and MIPS are each only part of the story -- true performance needs all three terms of the equation, or real execution time.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
31
Notes: Let's bring it all together. Four ideas to leave with today: first, the Basic Performance Equation itself, which you should be able to write from memory. Second, that CPI inflation has three named causes -- structural, data, and control hazards -- and a clean "frequency times penalty" formula. Third, that pipeline depth is a genuine engineering trade-off, not a free upgrade -- more stages is not automatically better. And fourth, the big-picture lesson: never trust a single number like clock speed or MIPS in isolation; always ask what it's leaving out.

## Slide 33
QUIZ — CSS2257
Quiz Questions
Q1 (MCQ): CPU Time is best expressed as: (a) IC + CPI + Clock Rate (b) IC × CPI × Clock Cycle Time (c) Clock Rate ÷ CPI (d) IC ÷ Clock Rate
Q2 (True/False): Increasing clock rate always increases overall processor performance.
Q3 (MCQ): A control hazard is caused by: (a) two instructions sharing hardware (b) an unresolved branch (c) a slow multiplier (d) low clock rate
Q4 (Short Answer): If Instruction Count doubles while CPI and clock rate stay fixed, what happens to CPU Time?
Q5 (True/False): A deeper pipeline always improves overall performance.
Q6 (Short Answer): Why is comparing MIPS across two different instruction set architectures misleading?
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
32
Notes: This is a knowledge check, not a graded exam -- tell students that up front to keep the pressure low. Give them about four minutes, working individually first, then let them briefly discuss with a neighbor before you reveal answers. Question 3 tests the hazard vocabulary from earlier; Questions 4 through 6 test whether the equation and its caveats have really sunk in, not just rote recall.

## Slide 34
QUIZ — CSS2257
Quiz Answers
A1: (b) CPU Time = IC × CPI × Clock Cycle Time — the Basic Performance Equation.
A2: False — only if CPI and Instruction Count stay the same; a higher clock rate with higher CPI can still be slower overall.
A3: (b) An unresolved branch — the pipeline doesn’t yet know which instruction to fetch next.
A4: CPU Time doubles — it is directly proportional to Instruction Count.
A5: False — deeper pipelines raise clock rate but also raise stall/flush penalties, which can raise CPI enough to offset the gain.
A6: Different ISAs do different amounts of work per instruction, so counting instructions per second compares incompatible units of "work."
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
33
Notes: Go through each answer briefly, and pause on any question where a show of hands reveals a lot of disagreement -- that's your signal for what to revisit in the next class. Question 2 and 5 are the two most commonly missed in practice, because they directly contradict the marketing intuition students walked in with -- circle back to the Megahertz Myth slide if needed. Encourage students to note down which questions they got wrong for their own revision, this isn't being graded.

## Slide 35
WHAT’S NEXT
Further Reading & Assignment
Further Reading
Hennessy & Patterson, "Computer Organization and Design" — chapters on performance and pipelining.
Assignment
Compute CPU Time and effective CPI for 2 given processors with stall data; submit before next session.
Coming Up Next
Superscalar execution and out-of-order pipelines — how CPI can drop below 1.
Presidency University, Bengaluru | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
34
Notes: To close: point students to the Hennessy & Patterson chapters for a deeper treatment with more rigor than we had time for today. Assign the CPU-time-and-CPI problem set so they get individual practice before it appears on an assessment. And tease next session -- once students are comfortable with CPI possibly exceeding 1, the natural next question is "can CPI go below 1?" -- which sets up superscalar and out-of-order execution perfectly. Thank the class and open the floor for questions.