## Slide 1
CSS2257 · COMPUTER ORGANIZATION AND ARCHITECTURE
Arithmetic Operations on
Signed Numbers
A Collaborative Learning Session
Think-Pair-Share • Jigsaw Groups • Peer Teaching
Presidency University | School of Artificial Intelligence and Advanced Computing
Department of AI & Robotics | Prof. Manoj Sagar
Notes: Welcome the class warmly. Today is a collaborative session — students will spend nearly as much time talking to each other as listening to you. Set expectations: they will work in pairs and small groups throughout, and by the end each of them should be able to explain overflow and 2's complement arithmetic to a classmate. Mention this mirrors how engineers actually work through tricky ALU design decisions — by talking it through with colleagues.

## Slide 2
Course & Session Details
UNIVERSITY
Presidency University, Bengaluru
SCHOOL
School of Artificial Intelligence and Advanced Computing
DEPARTMENT
Department of AI & Robotics
SUBJECT
Computer Organization and Architecture (CSS2257)
FACULTY
Prof. Manoj Sagar
SESSION FORMAT
Collaborative Learning — pairs, jigsaw groups, and peer teaching
Presidency University | CSS2257
1
Notes: This is the branding/logistics slide - keep it brief, under a minute, mainly for the record and for students who join late.

## Slide 3
Learning Objectives
Represent signed integers using sign-magnitude, 1’s complement, and 2’s complement.
Compute the representable range of an n-bit signed number.
Add and subtract signed numbers using 2’s complement arithmetic.
Detect overflow in signed addition and explain why it occurs.
Explain and defend these ideas to a peer — not just calculate them.
Presidency University | CSS2257
2
Notes: Read each objective aloud and tie it back to the icebreaker question they just discussed - by the end of the session they should be able to answer it precisely.

## Slide 4
Icebreaker: Think, Pair, Share
“If a computer only understands 0s and 1s, how do you think it represents a NEGATIVE number?”
THINK (1 min): Jot your own guess — no wrong answers yet.
PAIR (2 min): Compare guesses with your neighbor.
SHARE: 3–4 pairs share with the class.
Presidency University | CSS2257
3
Notes: Give students the full 1 minute of silent think time before letting them talk - resist the urge to rush to sharing.

## Slide 5
How We’ll Learn Today
Think-Pair-Share
Quick individual thought, then a partner check, before we discuss as a class.
Jigsaw Groups
Each small group becomes the expert on one piece, then teaches it to another group.
Peer Teaching
You explain a concept to a classmate — the fastest way to find out what you truly understand.
Presidency University | CSS2257
4
Notes: Explain that these three structures will repeat throughout the session so they know what to expect each time you introduce an activity.

## Slide 6
Why Signed Representation Matters
Every processor’s ALU must handle both positive and negative values — temperatures, bank balances, sensor offsets, error codes.
Hardware has no minus sign — only bit patterns. The representation scheme IS the design decision.
Real-time example: a drone’s altitude-change sensor reports +250 or −180 mm/s — the CPU only sees bits.
Get the representation wrong, and addition, comparison, and overflow checks all break.
Presidency University | CSS2257
5
Notes: Use a concrete, relatable example (drone sensor, bank balance) rather than an abstract one to hook interest before diving into bit patterns.

## Slide 7
Quick Recap: Unsigned Binary
An n-bit unsigned number represents values 0 to 2ⁿ − 1.
Example (4-bit): 0000 = 0, up to 1111 = 15.
Every bit is a magnitude bit — there is no sign information at all.
4-bit unsigned range
0000 → 0
1111 → 15
Question for today: how do we squeeze negative values into the same bit patterns?
Presidency University | CSS2257
6
Notes: Quickly poll the room: how many bits would be needed to represent numbers up to 100? This warms up their unsigned-binary recall before signed numbers.

## Slide 8
Representation 1: Sign-Magnitude
The most significant bit (MSB) is the sign bit: 0 = positive, 1 = negative.
The remaining n−1 bits hold the magnitude, exactly as in unsigned binary.
Example (4-bit): +5 = 0101, and −5 = 1101 (same magnitude, sign bit flipped).
Drawback: two representations for zero (0000 and 1000) — awkward for hardware.
Presidency University | CSS2257
7
Notes: Draw the 4-bit example on the board bit by bit as you talk through it so the sign bit placement is visually obvious.

## Slide 9
COLLABORATIVE TASK
Pair Practice — Sign-Magnitude Conversion
Work in pairs of 2
Partner A converts +9 and −11 to 5-bit sign-magnitude. Partner B converts −14 and +6. Then swap books and check each other’s work.
Write the magnitude in binary first, ignoring the sign.
Set the MSB to 0 (positive) or 1 (negative).
Cross-check your partner’s answer and agree on any disagreement before moving on.
Time: 4 minutes
Presidency University | CSS2257
8
Notes: Circulate while groups work. Listen for the specific misconception this task is designed to surface, and note down one or two group answers to reference when you debrief with the whole class.

## Slide 10
Representation 2: 1’s Complement
Positive numbers look identical to unsigned binary.
To negate a number, flip every bit (0↔1).
Example (4-bit): +5 = 0101 → −5 = 1010 (bitwise complement).
Still has two zeros: 0000 (+0) and 1111 (−0) — arithmetic needs an “end-around carry” fix.
Presidency University | CSS2257
9
Notes: Emphasize the mechanical bit-flip operation - have a student physically flip fingers up/down to represent flipping bits as a memory aid.

## Slide 11
COLLABORATIVE TASK
Jigsaw — 1’s Complement Conversion
Groups of 4 — each group gets ONE number
Group 1: convert +7. Group 2: convert −7. Group 3: convert +12. Group 4: convert −12 (use 5-bit width). Each group becomes the “expert” on its number.
Within your group, agree on the binary magnitude, then flip bits if negative.
Appoint one “expert speaker” to explain your group’s answer to the class.
As a class, verify that +7 and −7 are true bitwise complements of each other.
Time: 6 minutes
Presidency University | CSS2257
10
Notes: Circulate while groups work. Listen for the specific misconception this task is designed to surface, and note down one or two group answers to reference when you debrief with the whole class.

## Slide 12
Representation 3: 2’s Complement
Take the 1’s complement, then add 1 to the least significant bit.
Example (4-bit): +5 = 0101 → flip → 1010 → add 1 → 1011 = −5.
Only ONE representation for zero: 0000.
This is the scheme used by virtually every modern processor.
Presidency University | CSS2257
11
Notes: This is the payoff slide - many students find 2's complement 'clicks' here after seeing sign-magnitude and 1's complement first. Pause for questions.

## Slide 13
Group Discussion: Why 2’s Complement Wins
In your table group (4 min): list every advantage 2’s complement has over sign-magnitude and 1’s complement. Be ready to defend your top pick.
Hint: how many representations of zero does each scheme have?
Hint: does subtraction need special hardware, or can it reuse the adder?
Hint: what happens to the end-around carry problem?
Presidency University | CSS2257
12
Notes: Let the discussion run a little loose here; the goal is for students to construct the 'why' themselves rather than being told directly.

## Slide 14
COLLABORATIVE TASK
Speed Round — 2’s Complement Conversion
Pairs — first correct pair wins the round
Convert the following to 5-bit 2’s complement as fast (and correctly) as you can: +10, −15, +2, −1.
Shortcut: scan from the LSB, copy bits up to and including the first 1, then flip the rest.
Race your partner — but you must both agree on the final answers.
First pair with all four correct raises hands.
Time: 3 minutes
Presidency University | CSS2257
13
Notes: Circulate while groups work. Listen for the specific misconception this task is designed to surface, and note down one or two group answers to reference when you debrief with the whole class.

## Slide 15
Range of Representable Values (n-bit, 2’s Complement)
Bits (n) | Minimum | Maximum | Total Values
4 | −8 | +7 | 16
8 | −128 | +127 | 256
16 | −32,768 | +32,767 | 65,536
n | −2ⁿ⁻¹ | +2ⁿ⁻¹ − 1 | 2ⁿ
Notice the asymmetry: one more negative number than positive — because 0 only uses up one positive slot.
Presidency University | CSS2257
14
Notes: Point out the asymmetry (one extra negative value) explicitly - it's a classic exam question and easy to miss.

## Slide 16
COLLABORATIVE TASK
Jigsaw Report-Back — Bit-Width Ranges
Groups of 3 — each group owns one bit-width
Group A: derive the range for 6 bits. Group B: for 10 bits. Group C: for 12 bits. Show your working, not just the final numbers.
Use the formula: minimum = −2ⁿ⁻¹, maximum = 2ⁿ⁻¹ − 1.
Cross-check against the pattern in the table on the previous slide.
Send one member to a neighboring group to compare answers before the class report-back.
Time: 5 minutes
Presidency University | CSS2257
15
Notes: Circulate while groups work. Listen for the specific misconception this task is designed to surface, and note down one or two group answers to reference when you debrief with the whole class.

## Slide 17
Adding Signed Numbers (2’s Complement)
Add the bit patterns exactly like unsigned binary addition.
Discard any carry-out of the MSB — it is not part of the result.
The beauty: the SAME adder circuit works whether operands are positive or negative.
The only extra step is checking for overflow (coming up next).
Presidency University | CSS2257
16
Notes: Emphasize that this is the single biggest advantage of 2's complement: one adder circuit, no special-casing for sign.

## Slide 18
Worked Example 1: Positive + Positive
4-bit: 0011 (+3) + 0010 (+2)
Step 1: Add the bits as unsigned binary: 0011 + 0010 = 0101.
Step 2: No carry out of the MSB, so no overflow to worry about.
Step 3: Read the sign bit: 0 → positive. Decode the magnitude: 101 = 5.
Result: 0101 = +5 ✓ matches +3 + +2 = +5
Presidency University | CSS2257
17
Notes: Work through this example on the board step by step, but pause after each step and ask a student to predict the next one before you reveal it — keep it interactive even though it's a worked example.

## Slide 19
Worked Example 2: Positive + Negative
4-bit: 0110 (+6) + 1101 (−3)
Step 1: Add as unsigned binary: 0110 + 1101 = 10011 (5 bits produced).
Step 2: Discard the carry-out of the MSB → keep only 0011.
Step 3: Sign bit is 0 → positive, magnitude 011 = 3.
Result: 0011 = +3 ✓ matches +6 + (−3) = +3
Presidency University | CSS2257
18
Notes: Work through this example on the board step by step, but pause after each step and ask a student to predict the next one before you reveal it — keep it interactive even though it's a worked example.

## Slide 20
COLLABORATIVE TASK
Whiteboard Group Practice — Addition
Groups of 4 — one shared whiteboard per group
Compute, in 5-bit 2’s complement, on your group whiteboard: (a) +9 + (−4) (b) −7 + (−5) (c) +6 + (+6).
Everyone converts operands to binary before adding — check each other.
Circle the carry-out of the MSB on every sum; discuss whether it gets discarded.
Convert the final bit pattern back to decimal and sanity-check against normal arithmetic.
Time: 7 minutes
Presidency University | CSS2257
19
Notes: Circulate while groups work. Listen for the specific misconception this task is designed to surface, and note down one or two group answers to reference when you debrief with the whole class.

## Slide 21
What Is Overflow?
Overflow happens when the true mathematical result does not fit in the available bits.
It can only occur when adding two numbers of the SAME sign (both positive or both negative).
Adding a positive and a negative number can never overflow — the true result is always smaller in magnitude than the larger operand.
An incorrect sign in the result is the tell-tale symptom.
Presidency University | CSS2257
20
Notes: Ask the class for a real-life analogy of overflow before defining it formally - e.g. an odometer rolling over.

## Slide 22
The Overflow Detection Rule
Compare the carry INTO the sign bit with the carry OUT of the sign bit.
If the two carries differ → overflow has occurred.
If the two carries match → the result is valid, discard any carry-out as usual.
Equivalently: overflow occurs when two same-sign operands produce a result with the opposite sign.
Presidency University | CSS2257
21
Notes: Have students say the rule out loud in their own words before you show the formal carry-in/carry-out phrasing on screen.

## Slide 23
Worked Example: Overflow Case
4-bit: 0101 (+5) + 0100 (+4)
Step 1: Add as unsigned binary: 0101 + 0100 = 1001.
Step 2: Track the carries around the sign bit (bit 3): adding bit 2 (1+1) produces a carry INTO bit 3, but bit 3’s own addition (0+0+carry) produces NO carry OUT.
Step 3: Carry-in (1) ≠ carry-out (0) → the two carries differ → OVERFLOW has occurred.
⚠ Sign bit of 1001 reads as −7, not +9 — the 4-bit range (−8 to +7) cannot hold +9.
Presidency University | CSS2257
22
Notes: Work through this example on the board step by step, but pause after each step and ask a student to predict the next one before you reveal it — keep it interactive even though it's a worked example.

## Slide 24
COLLABORATIVE TASK
Gallery Walk — Spot the Overflow
Groups of 3, rotating between 4 posted problems
Four 4-bit addition problems are posted around the room. As a group, rotate to each, decide overflow YES/NO, and write your reasoning on a sticky note.
Problem stations: (1) 0110+0011 (2) 1010+1001 (3) 0111+0001 (4) 1100+1011.
Use the carry-comparison rule — show both carries on your sticky note.
After all rotations, compare your verdicts with the group that started elsewhere.
Time: 8 minutes (2 min/station)
Presidency University | CSS2257
23
Notes: Circulate while groups work. Listen for the specific misconception this task is designed to surface, and note down one or two group answers to reference when you debrief with the whole class.

## Slide 25
Subtraction via 2’s Complement Addition
Key idea: A − B = A + (−B).
Take the 2’s complement of B (flip bits, add 1), then add it to A using ordinary addition.
No separate subtractor circuit is needed — the same adder hardware is reused.
The same overflow rule from addition still applies to the result.
Presidency University | CSS2257
24
Notes: Draw the A - B = A + (-B) identity large on the board - this is the single most important idea in this section.

## Slide 26
Worked Example: Subtraction
4-bit: 0111 (+7) − 0010 (+2)
Step 1: Find −B: 2’s complement of 0010 → flip → 1101 → add 1 → 1110 (−2).
Step 2: Add A + (−B): 0111 + 1110 = 10101 (5 bits produced).
Step 3: Discard the carry-out of the MSB → keep 0101; carries into/out of sign bit match → no overflow.
Result: 0101 = +5 ✓ matches +7 − 2 = +5
Presidency University | CSS2257
25
Notes: Work through this example on the board step by step, but pause after each step and ask a student to predict the next one before you reveal it — keep it interactive even though it's a worked example.

## Slide 27
COLLABORATIVE TASK
Peer-Check Practice — Subtraction
Pairs — swap and grade each other
Individually solve, in 5-bit 2’s complement: (a) +10 − 6 (b) −4 − 9 (c) +3 − (−5). Then trade papers with your partner.
As the grader: verify every step — the 2’s complement of B, the addition, and overflow check.
Circle any step where you disagree and discuss until you reach consensus.
Flag any part you can’t explain to your partner — bring it to the class discussion.
Time: 6 minutes
Presidency University | CSS2257
26
Notes: Circulate while groups work. Listen for the specific misconception this task is designed to surface, and note down one or two group answers to reference when you debrief with the whole class.

## Slide 28
Common Misconceptions & Pitfalls
Myth: overflow can happen when adding a positive and a negative number. (False — impossible.)
Myth: a carry out of the MSB always means overflow. (False — it depends on matching it with the carry INTO the MSB.)
Myth: 1’s complement and 2’s complement negation are the same thing. (2’s complement adds 1 after flipping.)
Myth: the sign bit is separate from the value. (In 2’s complement, it carries real place-value weight: −2ⁿ⁻¹.)
Presidency University | CSS2257
27
Notes: Ask for a show of hands on which misconception they used to believe - normalizing the mistake helps students admit and correct it.

## Slide 29
Think-Pair-Share: Where Does This Matter?
With your partner (2 min): name ONE real system where signed-number overflow could cause a serious failure.
ALU design: every CPU’s arithmetic logic unit relies on this exact overflow rule.
Embedded/automotive sensors: a signed overflow in a speed or temperature reading can trigger false alarms or missed faults.
Famous case: the Ariane 5 rocket failure (1996) traced to an unhandled numeric overflow in flight software.
Presidency University | CSS2257
28
Notes: If time is short, this can be shortened to a single share-out rather than full pair discussion - but don't skip the Ariane 5 example.

## Slide 30
COLLABORATIVE TASK
Peer Teaching — Jigsaw Wrap-Up
New pairs — one from each side of the room
Pair up with someone you haven’t worked with today. Person 1 teaches “how to detect overflow” from scratch. Person 2 teaches “how 2’s complement subtraction works” from scratch. No notes for the first pass!
Teach using your own words and a simple example — pretend your partner has never seen this before.
Listener: ask at least one clarifying question.
Swap roles, then together write one sentence summarizing why 2’s complement is the industry standard.
Time: 6 minutes
Presidency University | CSS2257
29
Notes: Circulate while groups work. Listen for the specific misconception this task is designed to surface, and note down one or two group answers to reference when you debrief with the whole class.

## Slide 31
Summary of Key Points
Three representations exist: sign-magnitude, 1’s complement, 2’s complement — modern hardware uses 2’s complement.
n-bit 2’s complement range: −2ⁿ⁻¹ to +2ⁿ⁻¹ − 1, with a single representation of zero.
Addition is uniform for all signs; the carry-out of the MSB is simply discarded.
Overflow is detected by comparing the carry into and out of the sign bit — and can only happen for same-sign operands.
Subtraction reuses the adder: A − B = A + (2’s complement of B).
Presidency University | CSS2257
30
Notes: Read through the summary slowly - this is what they should carry into the quiz and into next week's session.

## Slide 32
Quiz — Check Your Understanding
Q1. Convert −13 to 5-bit 2’s complement.
Q2. True or False: Overflow can occur when adding +8 and −3.
Q3. What is the range of a signed 8-bit number?
Q4. Compute (4-bit): 0100 + 1011. State the decimal result.
Q5. Which representation has only one pattern for zero?
Q6. Compute +6 − 9 using 2’s complement addition (5-bit).
Work individually, 4 minutes — then compare with your neighbor before we reveal answers.
Presidency University | CSS2257
31
Notes: Do not reveal answers yet - let the neighbor-comparison step happen fully before moving to the next slide.

## Slide 33
Quiz Answers
A1. 10011 (13 = 01101 → flip → 10010 → +1 → 10011).
A2. False — opposite-sign addition can never overflow.
A3. −128 to +127 (256 total values).
A4. 0100+1011 = 1111 = −1 (no overflow: carries into/out of sign bit match).
A5. 2’s complement.
A6. +6 − 9 = 00110 + (2’s complement of 01001 = 10111) = 11101 = −3.
Presidency University | CSS2257
32
Notes: Go question by question; pause after each to let students self-correct before moving to the next.

## Slide 34
Exit Ticket: Reflection
On a sticky note, before you leave, write:
1) One thing you can now explain confidently.
2) One thing that still feels shaky.
3) One question you’d ask a classmate to help you check your understanding next class.
Hand your sticky note to a partner — they keep it and check in with you next session.
Presidency University | CSS2257
33
Notes: Collect the sticky notes physically if possible - they're useful for planning what to review at the start of next class.

## Slide 35
Further Reading & Group Assignment
Read: Carl Hamacher, “Computer Organization and Embedded Systems,” chapter on arithmetic and logic operations.
Read: Patterson & Hennessy, “Computer Organization and Design,” arithmetic-for-computers chapter.
GROUP ASSIGNMENT (submit as a team of 3): design an 8-bit adder-subtractor block diagram, including the overflow-detection logic, and be ready to present it next class.
Bring your sticky-note question from today’s exit ticket to compare with your teammates.
Presidency University | CSS2257
34
Notes: Assign groups for the assignment now if you haven't already, so students leave with their team already formed.