## Slide 1
PRESIDENCY UNIVERSITY, BENGALURU
School of Artificial Intelligence and Advanced Computing | Department of AI & Robotics
Memory System: Basic Concepts,
Semiconductor RAM Memories
Computer Organization and Architecture • CSS2257
Faculty: Mr. Manoj Sagar
Semester — | Academic Year 2026

## Slide 2
COMPUTER ORGANIZATION AND ARCHITECTURE
Institute & Department
Presidency University, Bengaluru
School of Artificial Intelligence and Advanced Computing
Department of Artificial Intelligence & Robotics
Course: CSS2257 — Computer Organization and Architecture
Presidency University, Bengaluru | CSS2257
2
Notes: Quick reminder of where we are — Computer Organization and Architecture, part of your AI & Robotics curriculum. Understanding memory hardware might feel far from 'AI,' but every model you train or deploy lives inside memory systems like the ones we're about to study.

## Slide 3
TODAY'S ROADMAP
Learning Objectives
Define memory and its role in a computer system
Explain the memory hierarchy and its speed–cost trade-off
Differentiate RAM from ROM, and SRAM from DRAM
Describe SRAM and DRAM cell structures
Solve basic memory addressing problems
Identify types of ROM and real-world uses
Presidency University, Bengaluru | CSS2257
3
Notes: Here is our roadmap. By the end of this lecture, you should be comfortable defining memory hierarchy, telling SRAM and DRAM apart, and solving simple address-line problems. Keep these in mind — we revisit all of them in the quiz.

## Slide 4
ICEBREAKER
Let's Talk Memory!
When you hear "memory," what comes to mind first?
Ever seen "8GB RAM" on a phone box? What did you think it meant?
Why does your laptop forget everything once unplugged?
If you built the "perfect" memory, what would you use it for?
Presidency University, Bengaluru | CSS2257
4
Notes: Ask Q1 first, take a couple of quick verbal answers. Then Q2 and Q3 by show of hands. Q3 is the real hook — it sets up volatile vs non-volatile. Transition: 'Great instincts — today we turn that intuition into precise engineering.'

## Slide 5
MOTIVATION
Why This Topic Matters
Every running program lives in memory
Memory speed — not the CPU — is often the real bottleneck
AI training relies on massive, fast memory (GPU VRAM, HBM)
Phones, laptops, cars, wearables all depend on memory design
Presidency University, Bengaluru | CSS2257
5
Notes: The CPU often sits idle waiting for data — this is the 'memory wall,' one of the biggest challenges in architecture. In AI or robotics you'll constantly fight memory bandwidth limits. Understanding this helps you write faster code and design better systems.

## Slide 6
BASIC CONCEPT
What Is Memory?
Hardware that stores binary data (0s and 1s) for the CPU
Stores both data and instructions
Organized as locations, each with a unique address
Each location holds a fixed number of bits — a word
Presidency University, Bengaluru | CSS2257
6
Notes: Think of memory like an apartment building — each apartment has a unique address, and holds a fixed amount of 'stuff,' the word size. The CPU goes directly to an address, like a mail carrier to apartment 402 — this is 'random access.'

## Slide 7
OVERVIEW
Memory Hierarchy
Registers
Fastest · Smallest · Costliest
Cache (SRAM)
Very fast · Small
Main Memory (DRAM)
Fast · Medium size
Secondary Storage (SSD/HDD)
Slower · Largest · Cheapest
Speed & Cost per bit ↓
Capacity ↓ (bottom→top)
Presidency University, Bengaluru | CSS2257
7
Notes: Registers at the top: blazing fast, only a handful. Moving down: cache, main memory, secondary storage. Each level down is slower but bigger and cheaper per byte. This layered design is a clever compromise.

## Slide 8
TRADE-OFF
Speed – Cost – Capacity
Faster memory = more expensive per byte = smaller capacity
Slower memory = cheaper per byte = larger capacity
No single technology gives fast + cheap + large together
The hierarchy exploits this trade-off intelligently
Presidency University, Bengaluru | CSS2257
8
Notes: A 1TB drive built entirely from register-speed memory would cost more than a house. So engineers use a little fast, expensive memory backed by more slow, cheap memory. This is the core idea behind the whole hierarchy.

## Slide 9
VOCABULARY
Key Memory Characteristics
Access time — time to read/write one word
Cycle time — minimum time between two operations
Capacity — total data memory can hold
Cost per bit — economic cost of storing one bit
Volatility — does data survive when power is removed?
Presidency University, Bengaluru | CSS2257
9
Notes: These five terms appear on every datasheet you will read. Access time vs cycle time: cycle time includes recovery time before the next operation. Volatility explains why your open apps vanish when you unplug your laptop.

## Slide 10
CLASSIFICATION
RAM vs. ROM
RAM — Read & Write, Volatile
ROM — Read-mostly, Non-volatile
RAM loses data when powered off; ROM retains it without power
Both are "random access" — any location reached directly, roughly constant time
RAM = working memory; ROM = permanent/firmware storage
Presidency University, Bengaluru | CSS2257
10
Notes: Now we can answer the icebreaker properly: apps vanish because RAM is volatile. ROM holds startup firmware — data that must survive power loss. Both are 'random access' because the CPU jumps directly to any address, unlike a sequential tape.

## Slide 11
RAM
Random Access Memory — The Concept
RAM is the CPU's primary working memory
Supports both read and write operations
Access time is roughly equal for any address
Two major types: Static RAM (SRAM) and Dynamic RAM (DRAM)
Presidency University, Bengaluru | CSS2257
11
Notes: RAM is where your OS and active data live while the computer runs. Not all RAM is built the same way internally — SRAM and DRAM trade off speed, cost, and complexity very differently. Let us look at both.

## Slide 12
PREVIEW
Types of RAM — SRAM vs. DRAM
SRAM — Fast, 6-transistor, no refresh
DRAM — Dense, 1T-1C, needs refresh
SRAM → faster, more expensive → used in cache
DRAM → slower, cheaper, denser → used in main memory
Presidency University, Bengaluru | CSS2257
12
Notes: SRAM is like a light switch that stays put until flipped; DRAM is like a leaky bucket you constantly top up. That leakiness is the source of almost every practical difference between the two — let us open up both cells.

## Slide 13
SRAM
Static RAM — Cell Structure
Word Line
Access Tr.
Access Tr.
Inverter 1
Inverter 2
Feedback loop holds the bit
Bit Line
Bit Line'
Six transistors (6T) per cell
Two cross-coupled inverters hold a stable 0 or 1
Two access transistors connect to word/bit lines
Retains its value as long as power is applied
Presidency University, Bengaluru | CSS2257
13
Notes: Two inverters wired so one's output feeds the other's input — a stable feedback loop, like two people constantly agreeing with each other. The other two transistors are just switches to the word and bit lines. No refresh needed — that's the 'static' in Static RAM.

## Slide 14
SRAM
SRAM — Characteristics & Use Cases
Very fast access time (nanoseconds)
No refresh circuitry → simpler control logic
Larger cell (6T) → lower density, higher cost/bit
Used in: CPU cache (L1/L2/L3), registers, buffers
Presidency University, Bengaluru | CSS2257
14
Notes: Because SRAM needs no refresh, it is extremely fast — exactly why cache, which must keep pace with the CPU clock, is built from SRAM. The trade-off is size: 6 transistors/bit takes a lot of chip area, so cache stays small while RAM scales to gigabytes.

## Slide 15
DRAM
Dynamic RAM — Cell Structure
Word Line
Transistor (switch)
Capacitor (stores charge)
Bit Line
One transistor + one capacitor (1T-1C) per cell
Charge on the capacitor: charged = 1, discharged = 0
Transistor switches the capacitor to the bit line
Far more compact than SRAM's 6-transistor design
Presidency University, Bengaluru | CSS2257
15
Notes: One transistor and one capacitor — a huge space saving over SRAM's six transistors, which is why DRAM packs so much more storage. The catch: capacitors leak charge like a bucket with a tiny hole. That leak is why DRAM needs refreshing.

## Slide 16
DRAM
DRAM — The Refresh Operation
Capacitors leak charge over time
Refresh: periodically read & rewrite each cell
Typical interval: ~64 ms for the whole chip
Handled automatically by the memory controller
Presidency University, Bengaluru | CSS2257
16
Notes: Every DRAM cell must be refreshed roughly every 64 ms or the charge decays too far. This background task is invisible to the programmer, but costs a little time and power — and is the single biggest architectural difference from SRAM.

## Slide 17
COMPARISON
SRAM vs. DRAM — Side by Side
Feature | SRAM | DRAM
Cell structure | 6 transistors | 1 transistor + 1 capacitor
Refresh needed? | No | Yes
Speed | Faster | Slower
Density / Capacity | Lower | Higher
Cost per bit | Higher | Lower
Typical use | Cache | Main memory
Presidency University, Bengaluru | CSS2257
17
Notes: This table is exam-favorite material. Every SRAM advantage (speed, no refresh) costs density and price, and vice versa for DRAM — a perfect example of the speed-cost-capacity trade-off from the hierarchy discussion.

## Slide 18
REAL-WORLD
RAM in Your Devices
Phone RAM — DRAM (LPDDR)
CPU Cache — SRAM (L1/L2/L3)
GPU Memory — GDDR6 / HBM
"8GB RAM" on a phone box = DRAM, a low-power variant
Cache sizes in CPU specs (L1/L2/L3) = SRAM, on-chip
Gaming/AI GPUs use specialized high-bandwidth DRAM
Presidency University, Bengaluru | CSS2257
18
Notes: Connect straight back to the icebreaker: '8GB RAM' is DRAM, a low-power variant for battery life. Cache sizes in laptop specs are SRAM. GPU memory (GDDR6/HBM) is specialized DRAM for very high bandwidth. You can now read a spec sheet.

## Slide 19
ORGANIZATION
Address Lines and Word Size
Capacity = (number of words) × (bits per word)
Address lines needed = log₂(number of words)
Data lines needed = word size (bits per word)
Notation: "1K × 8" = 1024 words, each 8 bits wide
Presidency University, Bengaluru | CSS2257
19
Notes: Address pins select WHICH word you want; data pins carry the bits in or out. Address lines = log base 2 of total words — asking 'how many binary digits to uniquely number every location?' Let's work an example.

## Slide 20
WORKED EXAMPLE
Finding Address Lines
Problem: A memory chip has capacity 1K × 8. Find the address and data lines.
Given: 1K words = 1024 words, 8 bits per word
Step 1
Address lines = log₂(1024)
Step 2
2¹⁰ = 1024, so 10 address lines
Step 3
Data lines = word size = 8 bits
Answer: 10 address lines, 8 data lines
Presidency University, Bengaluru | CSS2257
20
Notes: Understand what is given: 1024 locations, 8 bits each. Since 2 to the 10 equals 1024, we need exactly 10 address lines. Data lines simply equal the word size, 8. Address lines answer "which location"; data lines answer "how much data per access."

## Slide 21
WORKED EXAMPLE
A Larger Chip
Problem: A memory chip is 64K × 16. Find the address and data lines.
Given: 64K words = 65,536 words, 16 bits per word
Step 1
Address lines = log₂(65,536)
Step 2
2¹⁶ = 65,536, so 16 address lines
Step 3
Data lines = word size = 16 bits
Answer: 16 address lines, 16 data lines
Presidency University, Bengaluru | CSS2257
21
Notes: "K" in memory notation is always 1024, not exactly 1000, so 64K = 65,536. Since 2 to the 16 equals 65,536, 16 address lines. Quick check: if the chip were 64K × 32, address lines stay 16, but data lines become 32 — this trips people up on exams.

## Slide 22
INTERNAL ORGANIZATION
Inside a Memory Chip
Address In
Decoder
Memory
Cell Array
Data Out
CS · R/W Control
Decoder converts the binary address to select one word
Chip Select (CS) activates the chip when addressed
Read/Write (R/W) line sets the operation type
Together they turn an address into real electrical signals
Presidency University, Bengaluru | CSS2257
22
Notes: The decoder is the traffic director — it activates exactly one row out of thousands. Chip Select says "you are the one being addressed" when multiple chips share a bus. R/W tells the chip whether this is a read or a write.

## Slide 23
EXPANSION
Increasing Word Size
Chip 1
4-bit
Chip 2
4-bit
Chip 3
4-bit
Chip 4
4-bit
Shared Address Bus
Combined 16-bit Data Bus
Connect chips in parallel, sharing the same address lines
Each chip contributes some bits of the total word
Four 4-bit chips combine into a 16-bit-wide memory
Address lines stay the same; data lines multiply
Presidency University, Bengaluru | CSS2257
23
Notes: Chips share the exact same address lines, so they always point at the same row simultaneously — but each contributes a slice of the final word, like four musicians each playing their own instrument's part of one chord.

## Slide 24
EXPANSION — WORKED EXAMPLE
Increasing Capacity
Chip 1 — 1K × 8
Chip 2 — 1K × 8
Chip 3 — 1K × 8
Chip 4 — 1K × 8
2-to-4
Decoder
2 extra address lines
Need 4K × 8 memory, have 1K × 8 chips: 4096 ÷ 1024 = 4 chips
Each chip needs log₂(1024) = 10 address lines internally
log₂(4) = 2 extra lines select which chip is active
Total: 10 + 2 = 12 address lines for the whole system
Presidency University, Bengaluru | CSS2257
24
Notes: Word size stays 8 bits, but we need more total words, so we stack chips. 4096/1024 = 4 chips. Each chip needs 10 lines internally. Two extra lines, decoded by a small 2-to-4 decoder, pick which chip is active. 10 + 2 = 12 total.

## Slide 25
ROM FAMILY
Types of ROM
1
MROM
Set at manufacture, permanent
2
PROM
Written once by the user
3
EPROM
Erased using UV light
4
EEPROM
Erased electrically, byte by byte
5
Flash
Erased in blocks — USB, SSD
Presidency University, Bengaluru | CSS2257
25
Notes: Each ROM variant solves "how do we change it later" differently. Mask ROM never changes. PROM is written once. EPROM needed UV light to erase — genuinely. EEPROM erases electrically byte by byte. Flash erases in large blocks for speed.

## Slide 26
COMMON MISCONCEPTIONS
Myth vs. Fact
Myth
ROM can never be changed at all
Fact
EPROM, EEPROM, and Flash can be rewritten
Myth
More RAM always means a faster computer
Fact
RAM aids multitasking; CPU & storage speed matter too
Myth
SRAM and DRAM are just different sizes
Fact
They use entirely different storage mechanisms
Myth
RAM and storage (SSD/HDD) are the same
Fact
RAM is volatile working memory; storage is permanent
Presidency University, Bengaluru | CSS2257
26
Notes: "Read-Only Memory" sounds absolute, but several ROM types are rewritable — a historical name, not a strict rule. Adding RAM will not fix a slow CPU or disk. Never confuse RAM with storage — this single mix-up costs the most exam marks.

## Slide 27
QUICK CHECK
Mini Activity
In pairs, discuss for 2 minutes:
"Would you use SRAM or DRAM for a self-driving car's main working memory? Why?"
Think about: cost, capacity, speed, power consumption
Presidency University, Bengaluru | CSS2257
27
Notes: No single correct answer — the point is weighing trade-offs like an engineer. Large sensor/AI data pushes toward DRAM for main memory; time-critical control loops might use small SRAM caches. Ask a couple of pairs to share their reasoning.

## Slide 28
INDUSTRY EXAMPLE
Memory in Embedded & IoT Systems
Wearables — Flash + small SRAM
IoT Sensors — EEPROM/Flash firmware
Automotive ECUs — reliable non-volatile
Engineers agonize over every extra kilobyte (cost, battery life)
Firmware lives in Flash/EEPROM — must survive power loss
A little SRAM handles temporary, real-time calculations
Presidency University, Bengaluru | CSS2257
28
Notes: This is where memory concepts enter real products, especially in AI & Robotics. Embedded devices are resource-constrained — extra kilobytes cost battery and money. If you build an IoT project this semester, you will make exactly these trade-off decisions.

## Slide 29
RECAP
Summary of Key Points
Memory hierarchy balances speed, cost, and capacity
RAM (volatile) vs. ROM (non-volatile); both random access
SRAM: 6T latch, fast, no refresh, used in cache
DRAM: 1T-1C, needs refresh, used in main memory
Address lines = log₂(words); data lines = word size
ROM family: MROM → PROM → EPROM → EEPROM → Flash
Presidency University, Bengaluru | CSS2257
29
Notes: We started with the big picture — the hierarchy — and zoomed to individual transistors. We calculated address/data lines and expanded memory in width and capacity. Check off each learning objective from Slide 3 — any quick questions before the quiz?

## Slide 30
CHECK YOUR UNDERSTANDING
Quiz — Memory Systems
Q1. Which RAM type needs no refreshing? (a) DRAM (b) SRAM (c) EEPROM (d) Flash
Q2. True/False: ROM is always completely unchangeable after manufacture.
Q3. A DRAM cell uses: (a) 6 transistors (b) 1 transistor + 1 capacitor (c) 4 transistors
Q4. A chip is specified as 2K × 8. How many address lines does it need?
Q5. Which memory type is used for CPU cache? (a) DRAM (b) SRAM (c) EEPROM
Q6. True/False: RAM and secondary storage (SSD/HDD) are the same thing.
Q7. Name one real-world device that uses Flash memory for firmware.
Presidency University, Bengaluru | CSS2257
30
Notes: Give everyone ~4 minutes, individually or in pairs. This is for their own understanding, not grading. Q1/Q5 test SRAM/DRAM, Q2 tests the ROM misconception, Q3 tests cell structure, Q4 applies the address-line formula, Q6/Q7 test real-world understanding.

## Slide 31
ANSWERS
Quiz Answers — Memory Systems
A1. (b) SRAM — holds data via transistor feedback, no leaking capacitor
A2. False — EPROM, EEPROM, and Flash are rewritable
A3. (b) 1 transistor + 1 capacitor — gives DRAM its high density
A4. log₂(2048) = 11 address lines
A5. (b) SRAM — chosen for speed to match the CPU
A6. False — RAM is volatile working memory; storage is permanent
A7. e.g. smartphone, USB drive, SSD, smart thermostat firmware
Presidency University, Bengaluru | CSS2257
31
Notes: Walk Q4 live: 2K = 2048 words, 2¹¹ = 2048, so 11 address lines — same method as Slides 20-21. Pay special attention to Q2 and Q6, our two myth-vs-fact items — if many got these wrong, revisit volatility and rewritability next class.