## Slide 1
PRESIDENCY UNIVERSITY, BENGALURU
School of Artificial Intelligence and Advanced Computing | Department of AI & Robotics
Internal Organization of Memory Chips:
Capacity Calculation, Word & Bit Organization
Computer Organization and Architecture • CSS2257
Faculty: Mr. Manoj Sagar
Semester — | Academic Year 2026

## Slide 2
COMPUTER ORGANIZATION AND ARCHITECTURE
Institute & Department
Presidency University, Bengaluru
School of Artificial Intelligence and Advanced Computing
Department of Artificial Intelligence & Robotics
Course: CSS2257 — Computer Organization and Architecture
Presidency University, Bengaluru | CSS2257
2
Notes: Quick reminder of the course context. Everything today builds directly on last class’s RAM/ROM/SRAM/DRAM foundation, so flag now if any of that felt shaky before we build on top of it.

## Slide 3
TODAY'S ROADMAP
Learning Objectives
Describe a memory chip’s internal organization
Distinguish word organization from bit organization
Calculate capacity from address and data line counts
Convert between total capacity, word count, and word size
Design a 2D (row-column) decoder layout
Solve chip-combination problems (width and capacity)
Presidency University, Bengaluru | CSS2257
3
Notes: This is a very calculation-heavy lecture — keep a calculator handy. Everything here is exam-critical and genuinely useful for reading hardware datasheets.

## Slide 4
ICEBREAKER
Chip Detective
If you saw "256M × 8" on a chip, what do those numbers mean?
Why organize memory as a grid instead of one long line?
Ever seen memory chips inside an old computer or phone?
Guess: how many memory cells are inside an 8GB RAM stick?
Presidency University, Bengaluru | CSS2257
4
Notes: Ask Q1 and let students guess without correcting yet. Q2 sets up row-column decoding. For Q4, the real answer is over 68 billion cells — the gap between guesses and reality is a great hook. Transition: "Today we build up to calculating that exact number ourselves."

## Slide 5
MOTIVATION
Why This Topic Matters
Every RAM upgrade decision depends on capacity math
Chip designers must minimize address-decoding hardware
Engineers combine chips to hit exact capacity/width targets
The most heavily tested numerical topic in this unit
Presidency University, Bengaluru | CSS2257
5
Notes: A "16GB" RAM stick isn’t an arbitrary number — it’s built from a specific number of chips with a specific internal organization. This also happens to be where most numerical exam questions in this course come from.

## Slide 6
RECAP
What We Know So Far
Memory = collection of addressable storage locations
Each location holds a fixed-size word
Address lines select a location; data lines carry the word
Address lines needed = log₂(number of words)
Presidency University, Bengaluru | CSS2257
6
Notes: Quick recap before we go deeper. You already know the basic formula. Today we unpack exactly how it translates into physical layout inside the chip, and push the arithmetic much further.

## Slide 7
BIG PICTURE
Inside a Memory Chip
Address In
Decoder
Memory
Cell Array
Data Out
CS · R/W Control
Four blocks: Decoder, Cell Array, R/W Control Logic, I/O Buffers
Decoder: turns a binary address into "select exactly one location"
Cell array: physically holds the bits
I/O buffers: hand data back out once found
Presidency University, Bengaluru | CSS2257
7
Notes: Think of a memory chip like a library. The cell array is the shelves. The decoder is the librarian who walks straight to the right shelf given a catalog number. The I/O buffers are the front desk, handing you the book once found.

## Slide 8
ADDRESS DECODER
How Selection Works
n-to-2^n
Decoder
n address
bits in
···
···
Active word
···
···
···
2^n outputs — only one active
Takes an n-bit binary address as input
Produces 2ⁿ output lines — exactly one goes active
Only the active line enables its word for read/write
Called an n-to-2ⁿ decoder
Presidency University, Bengaluru | CSS2257
8
Notes: A decoder is pure combinational logic — feed it a binary code, exactly one output activates. A 10-bit address needs a 10-to-1024 decoder. Decoder outputs always equal the number of words, since each output selects one word.

## Slide 9
WORKED EXAMPLE
Decoder Sizing
Problem: A memory has 1024 words. Find the decoder inputs and outputs.
Given: 1024 words
Step 1
Outputs = number of words = 1024
Step 2
Inputs = log₂(1024)
Step 3
2¹⁰ = 1024, so 10 inputs
Answer: 10-to-1024 decoder (10 inputs, 1024 outputs)
Presidency University, Bengaluru | CSS2257
9
Notes: Same math as address lines, framed differently. 1024 locations need 1024 decoder outputs, one per location. Since 2 to the 10 is 1024, 10 input bits. Decoder inputs = address lines — same number, two names.

## Slide 10
LIMITATION
1D (Linear) Decoding
Simplest approach: one decoder selects the word directly
Works fine for small memories (e.g., 1K words)
Problem: for large memories, the decoder becomes enormous
A 1M-word memory needs a 20-to-1,048,576 decoder — impractical
Presidency University, Bengaluru | CSS2257
10
Notes: A single decoder works on paper, but a decoder with over a million output lines eats enormous chip area and power. Real chips almost never do this for large memories. Engineers use a smarter 2D approach instead.

## Slide 11
SOLUTION
Two-Dimensional (Row-Column) Decoding
Column Decoder
Row
Decoder
Selected cell
(row ∩ column)
Split the address into a row address and a column address
A row decoder selects one row; a column decoder selects one column
The cell at the intersection is the selected location
Dramatically reduces decoder size and chip area
Presidency University, Bengaluru | CSS2257
11
Notes: This answers the icebreaker. Instead of one giant decoder, use two small ones — the selected cell is wherever the active row and column lines cross. Just like coordinates on a graph: no million labels, just an x and a y.

## Slide 12
WORKED EXAMPLE
Row-Column Decoder Sizing
Problem: A 1M-word memory is a 1024 × 1024 array. Size the decoders.
Given: 1024 rows × 1024 columns = 1,048,576 words
Step 1
Rows = 1024 → row decoder = 10-to-1024
Step 2
Columns = 1024 → column decoder = 10-to-1024
Step 3
Total: two 10-to-1024 decoders (20 address bits)
Answer: 20 address bits total, vs. one impractical 20-to-1,048,576 decoder
Presidency University, Bengaluru | CSS2257
12
Notes: Same total address space as Slide 10’s impractical case, but now built from two modest 10-to-1024 decoders. Same total address bits, vastly simpler hardware — this is why real DRAM chips use row/column addressing.

## Slide 13
CORE FORMULA
Memory Capacity
Capacity (bits) = (number of words) × (bits per word)
Number of words = 2^(number of address lines)
Written as "words × bits" — e.g., "4K × 8"
Bytes = bits ÷ 8
Presidency University, Bengaluru | CSS2257
13
Notes: This is the single most important formula today — write it down. Capacity is how many locations, multiplied by bits per location. Everything else today is a variation of this one idea.

## Slide 14
WORKED EXAMPLE
Basic Capacity Calculation
Problem: A chip is organized as 4K × 8. Find total capacity in bits and bytes.
Given: 4K words = 4096 words, 8 bits per word
Step 1
Capacity = 4096 × 8 = 32,768 bits
Step 2
32,768 ÷ 8 = 4096 bytes
Step 3
4096 bytes = 4 KB
Answer: 32,768 bits = 4 KB
Presidency University, Bengaluru | CSS2257
14
Notes: Since the word size is exactly 8 bits (1 byte), byte capacity equals word count directly — 4096 words = 4096 bytes. This won’t always be this clean, so let’s try a case where it isn’t.

## Slide 15
WORKED EXAMPLE
Capacity with a Wider Word
Problem: A chip is organized as 2K × 16. Find total capacity in bits and bytes.
Given: 2K words = 2048 words, 16 bits per word
Step 1
Capacity = 2048 × 16 = 32,768 bits
Step 2
32,768 ÷ 8 = 4096 bytes
Step 3
Same total as 4K × 8!
Answer: 32,768 bits = 4 KB — identical capacity, different organization
Presidency University, Bengaluru | CSS2257
15
Notes: 4K × 8 and 2K × 16 are completely different internal organizations that store exactly the same total data. Capacity alone doesn’t tell you everything about a chip — word width matters just as much for how it’s used.

## Slide 16
ORGANIZATION TYPES
Word Organization vs. Bit Organization
Word-organized — full word per address
Bit-organized — 1 bit per address
Bit-organized chips are combined side-by-side to build wider words
Word-organized chips are simpler to use
Bit-organized chips offer flexible widths
Presidency University, Bengaluru | CSS2257
16
Notes: A "1M × 8" chip is word-organized — one address gives 8 bits at once. A "1M × 1" chip is bit-organized — one address gives exactly 1 bit; you’d need 8 of these in parallel to build a byte-wide memory.

## Slide 17
WORKED EXAMPLE
Bit-Organized Chip Combination
Bit 1
Bit 2
Bit 3
Bit 4
Bit 5
Bit 6
Bit 7
Bit 8
Shared Address Bus
Combined Data Bus
Build 64K × 8 memory using 64K × 1 (bit-organized) chips
Need 8 chips — one per bit position — for an 8-bit word
All 8 chips share the same address lines
log₂(65536) = 16 address lines shared across all
Presidency University, Bengaluru | CSS2257
17
Notes: Every chip receives the exact same address at the same time — each asked "give me your bit for word 12345." Chip 0 supplies bit 0, chip 1 supplies bit 1, and so on — together they produce one full 8-bit word.

## Slide 18
REAL-WORLD
Why Bit Organization Still Matters
Legacy PCs (1980s-90s) — 1-bit DRAM
ECC Memory — narrow chips for flexibility
Modern DRAM — word-organized
Old motherboards covered in many tiny identical chips = bit-organized
Modern memory consolidated to word-organized chips
The underlying math applies identically either way
Presidency University, Bengaluru | CSS2257
18
Notes: If you’ve seen an old motherboard covered in many tiny identical chips, that’s likely bit-organized memory. Modern memory moved to word-organized chips because it’s simpler to route and faster to access.

## Slide 19
REVERSE DIRECTION
Capacity — Working Backwards
Sometimes given total capacity + word size, must find address lines
Step 1: Divide total capacity by word size to get word count
Step 2: Take log₂ of that word count
Same formula, opposite direction
Presidency University, Bengaluru | CSS2257
19
Notes: Exam questions love flipping the formula — instead of giving words and bits and asking for capacity, they give total capacity and ask for address lines. Same relationship, solved in a different order.

## Slide 20
WORKED EXAMPLE
Working Backwards from Capacity
Problem: A chip has 65,536 bits total, word size 8 bits. Find words and address lines.
Given: 65,536 bits, 8 bits/word
Step 1
Words = 65,536 ÷ 8 = 8192
Step 2
Address lines = log₂(8192)
Step 3
2¹³ = 8192, so 13 lines
Answer: 8192 words (8K), 13 address lines
Presidency University, Bengaluru | CSS2257
20
Notes: Divide total bits by word size first to recover word count — that undoes the multiplication. Then take log₂ for address lines. Students who skip the division and take log₂ of the raw bit count get the wrong answer — watch for that trap.

## Slide 21
WORKED EXAMPLE
Full Chip Specification
Problem: A chip has 12 address lines and 16 data lines. Give its full spec and capacity.
Given: 12 address lines, 16 data lines
Step 1
Words = 2¹² = 4096
Step 2
Word size = 16 bits (from data lines)
Step 3
Spec: 4096 × 16 = 65,536 bits = 8 KB
Answer: "4K × 16" — 8192 bytes total
Presidency University, Bengaluru | CSS2257
21
Notes: This starts from pin counts, exactly how you’d approach a real datasheet. Address lines give word count via 2 to that power; data lines directly give word size. Multiply for total capacity — your general-purpose toolkit.

## Slide 22
CAPACITY EXPANSION
Combining Chips — Recap
Goal: build a bigger memory than one chip can hold
Word size stays the same; only total word count increases
Requires extra address lines to select which chip is active
Extra lines = log₂(number of chips), via a small external decoder
Presidency University, Bengaluru | CSS2257
22
Notes: We touched on this last class — today we formalize the math fully. Stack multiple identical chips and use a small decoder to pick which chip is "listening," while the chip’s own address lines pick the word within it.

## Slide 23
WORKED EXAMPLE
Full Capacity Expansion
Chip 1 — 2K × 8
Chip 2 — 2K × 8
Chip 3 — 2K × 8
Chip 4 — 2K × 8
Decoder
2 extra address lines
Design an 8K × 8 memory using 2K × 8 chips
Chips = 8192 ÷ 2048 = 4
Address lines per chip = log₂(2048) = 11
Total: 11 + log₂(4) = 11 + 2 = 13 address lines
Presidency University, Bengaluru | CSS2257
23
Notes: Figure out chip count by dividing total words by per-chip words. Find each chip’s own address lines. Find the extra "which chip" lines via log₂ of chip count. Add the two counts together for the system total — 13 here.

## Slide 24
COMBINED EXPANSION
Word-Size AND Capacity Expansion
B1·W1
B1·W2
B1·W3
Bank 1
B2·W1
B2·W2
B2·W3
Bank 2
B3·W1
B3·W2
B3·W3
Bank 3
each row = word-size expansion · stacked rows = capacity expansion
Some designs need wider words AND more total words than one chip offers
Build "banks" — each bank is word-size-expanded, then stack banks
Total chips = (chips per bank) × (number of banks)
Presidency University, Bengaluru | CSS2257
24
Notes: Picture a grid: each row is a "bank" forming one wide word (word-size expansion), and you stack multiple rows for more total capacity (capacity expansion). Total chip count is simply rows times columns.

## Slide 25
WORKED EXAMPLE
Combined Expansion
Problem: Build a 16K × 16 memory using 4K × 8 chips.
Given: need 16K × 16, have 4K × 8 chips
Step 1
Width: 16 ÷ 8 = 2 chips per bank
Step 2
Capacity: 16K ÷ 4K = 4 banks
Step 3
Total chips: 2 × 4 = 8
Step 4
Address lines: log₂(4096)=12 + log₂(4)=2 → 14
Answer: 8 chips, 14 address lines total
Presidency University, Bengaluru | CSS2257
25
Notes: This is the challenge problem from last class — let’s solve it properly. Two chips side by side give the 16-bit width; four such pairs stacked give the 16K depth. Eight chips total, 14 address lines.

## Slide 26
COMMON MISCONCEPTIONS
Myth vs. Fact
Myth
More address lines always means more chips
Fact
Address lines depend on total words, not chip count
Myth
Capacity in bits and bytes are interchangeable
Fact
Always divide by 8 to convert bits to bytes
Myth
Word- and bit-organized chips store different amounts
Fact
Organization differs; total capacity can be identical
Myth
"K" in memory always means exactly 1000
Fact
In memory context, K = 1024 (2¹⁰)
Presidency University, Bengaluru | CSS2257
26
Notes: The K = 1024 confusion is the single most common arithmetic mistake in this topic — using 1000 instead of 1024 breaks your log₂ calculations. Always use powers of 2 for K, M, G in this course.

## Slide 27
QUICK CHECK
Mini Activity
In pairs, spend 2 minutes on this problem:
A chip is specified as 512K × 4. Find total capacity in bytes,
and how many chips to build a 2M × 4 memory.
Presidency University, Bengaluru | CSS2257
27
Notes: Give students 2 minutes to attempt this fully — it combines capacity calculation and chip combination in one problem. After time is up, ask a pair to share their steps out loud, not just the final answer.

## Slide 28
INDUSTRY EXAMPLE
Reading a Real Datasheet
Real DRAM chips are labeled like "512Mb × 8" or "2Gb × 16"
"Mb"/"Gb" mean megabits/gigabits — not bytes!
"512Mb × 8": 512M words × 8 = 4Gb = 512MB
Engineers convert bit-capacity to byte-capacity constantly
Presidency University, Bengaluru | CSS2257
28
Notes: A genuine industry gotcha — manufacturers specify chip capacity in bits (lowercase "b"), while consumers think in bytes (capital "B"). An 8GB module is built from chips rated in gigabits, not gigabytes.

## Slide 29
RECAP
Summary of Key Points
Internal organization: decoder + cell array + control + I/O
Large memories use row-column (2D) decoding
Capacity = words × bits/word; divide by 8 for bytes
Word- vs. bit-organized chips can share identical capacity
Combine chips by width, by capacity, or both
Always use powers of 2 for K, M, G
Presidency University, Bengaluru | CSS2257
29
Notes: We went from physical chip layout, through the core capacity formula, into word vs. bit organization, and finished with full system-design problems. Check each objective from Slide 3 — any questions before the quiz?

## Slide 30
CHECK YOUR UNDERSTANDING
Quiz — Memory Organization & Capacity
Q1. A memory with 2048 words needs how many address lines? (a) 9 (b) 10 (c) 11
Q2. A chip is 8K × 16. Find its total capacity in bytes.
Q3. Row-column decoding is used mainly to: (a) increase speed (b) reduce decoder size
Q4. True/False: A "1M × 1" chip is word-organized.
Q5. You need 4K × 8 memory but have only 1K × 8 chips. How many chips?
Q6. In memory context, 1K equals: (a) 1000 (b) 1024 (c) 1,000,000
Q7. A datasheet lists "256Mb". How many megabytes is that?
Presidency University, Bengaluru | CSS2257
30
Notes: Give students about 5 minutes — this is a longer quiz since today was calculation-heavy. Q1/Q6 test the address-line formula and K=1024 rule, Q2 tests capacity calculation, Q3 tests row-column decoding, Q4 is a trick (a ×1 chip is bit-organized, so False), Q5 tests capacity expansion, Q7 tests the bits-vs-bytes gotcha.

## Slide 31
ANSWERS
Quiz Answers — Organization & Capacity
A1. log₂(2048) = 11 → (c) 11
A2. 8192 × 16 = 131,072 bits ÷ 8 = 16,384 bytes = 16 KB
A3. (b) reduce decoder size — avoids one enormous single decoder
A4. False — a "×1" chip is bit-organized, not word-organized
A5. 4096 ÷ 1024 = 4 chips
A6. (b) 1024 — memory always uses powers of 2 for K/M/G
A7. 256Mb ÷ 8 = 32 MB
Presidency University, Bengaluru | CSS2257
31
Notes: Walk Q1 live: 2048 words needs log₂(2048), and since 2¹¹ = 2048, the answer is 11 — an easy off-by-one to make with powers of 2, so remind students to double-check by recomputing 2 to the power they chose. Pay extra attention to Q4 and Q7 — the two "gotcha" items testing careful reading.

## Slide 32
WHAT'S NEXT
Further Reading & Next Class
Next topic: Cache Memory — Mapping Techniques
Reading: Hamacher, Computer Organization — Memory Systems chapter
Try it: find a real DRAM datasheet, identify its row/column organization
Challenge: design a 32K × 32 memory using 8K × 8 chips
Presidency University, Bengaluru | CSS2257
32
Notes: Excellent work today — this was dense and calculation-heavy, and you handled it well. Next class we move to cache mapping, which builds on today’s addressing concepts. For homework, try finding a real datasheet online. See you next class!