## Slide 1
Internal Organization of Memory Chips
& Cache Memory Mapping Techniques
CSS2257 — Computer Organization and Architecture
Presidency University
School of Artificial Intelligence and Advanced Computing | Department of AI & Robotics
Faculty: Manoj Sagar
Notes: Welcome everyone to today's session. Today we're going deep into two closely related ideas that sit right at the heart of how computers store and retrieve information quickly: how memory chips are organized internally, and how the cache — a small, fast memory — decides where to place data borrowed from main memory. By the end of this hour, you'll be able to look at a memory chip's pin count and tell me its capacity, and you'll be able to work out, by hand, which cache line a given memory address maps to. Let's get started.

## Slide 2
Presidency University
School of Artificial Intelligence and Advanced Computing
Department of AI & Robotics
"Building strong foundations in computing systems"
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
2
Notes: Just a quick note on where this fits in your program. Computer Organization and Architecture is a foundation course — everything you learn here about how hardware actually stores and moves data will resurface later in AI and robotics courses, especially when we talk about why some models run faster on certain hardware. So treat today's topic as infrastructure knowledge that will pay off repeatedly.

## Slide 3
Learning Objectives
Explain how a memory chip is internally organized (address lines, data lines, decoders)
Calculate a memory chip's capacity and pin requirements
Explain why cache memory exists (the memory hierarchy)
Compare direct, fully associative, and set-associative mapping
Solve numerical problems on cache address mapping
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
3
Notes: Here's our roadmap for the hour. We'll start with the "inside" of a single memory chip — think of it like opening up the hood of a car. Then we'll zoom out to the bigger picture of why cache memory exists at all, and finally get hands-on with the three main ways cache decides where to store data. By the end, these five objectives should all feel comfortable, and you'll be ready for the quiz at the end.

## Slide 4
Warm-Up — A Few Quick Questions
Q1
When your laptop feels "slow," what do you think is actually happening inside it?
Q2
Have you ever noticed an app opens faster the second time you use it? Why might that be?
Q3
If you needed the same 5 books every day, would you check them out fresh each time, or keep them on your desk?
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
4
Notes: Let's warm up before diving into the technical content. Ask Q1 and take two or three quick verbal answers — don't correct them yet, just collect ideas. Then ask Q2 and let a couple of students respond; most will intuitively say "it's saved somewhere" — that's exactly the caching intuition we're building toward. For Q3, the "keep it on your desk" answer is the perfect analogy for cache: keeping frequently used data close by instead of fetching it from far away every single time. Use these three questions as a bridge — tell students, "Everything you just guessed at is what we're going to formalize today."

## Slide 5
Why This Topic Matters
Every program you write eventually becomes bits stored in memory chips
CPUs are extremely fast; main memory (DRAM) is comparatively slow — the "memory wall"
Cache mapping decisions directly affect real-world speed: gaming, ML training, browsing
Exam & interview favorite: cache-mapping numericals appear constantly in GATE and placements
Speed Gap
CPU (very fast)
DRAM (slow)
Cache sits between the two — small, fast, and placed right next to the CPU to bridge this gap.
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
5
Notes: Why should you care about something as "low-level" as memory chip pins and cache mapping? Two reasons. First, practically: this exact gap between a blazing-fast CPU and comparatively sluggish main memory is why cache exists at all, and understanding it helps you write faster code later, especially in AI workloads where memory access patterns can make or break performance. Second, practically for your careers: cache mapping numericals are extremely common in technical interviews and competitive exams. So today isn't just theory — it's exam-relevant and career-relevant.

## Slide 6
What Is a Memory Chip?
An integrated circuit that stores binary data (0s and 1s)
Organized as an array of memory cells, each cell storing 1 bit
Two main types: RAM (volatile) and ROM (non-volatile)
Every memory chip exposes three connection types: address lines, data lines, control lines
Address lines
Which location?
Data lines
What value?
Control lines
Read/Write? Active?
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
6
Notes: Let's build from the ground up. A memory chip, physically, is just a tiny piece of silicon packed with millions (or billions) of memory cells, where each cell can hold a single bit. Don't worry about the electronics of how a cell stores a bit — for this course, what matters is how we access that stored data from outside the chip. And for that, every memory chip exposes three kinds of connections: address lines that say "which cell do I want," data lines that carry the actual bit values in or out, and control lines that say "read or write, and are you even talking to me right now."

## Slide 7
Address Lines & Chip Capacity
Address lines determine how many unique locations can be addressed
n address lines → 2ⁿ addressable locations
Example: 10 address lines → 2¹⁰ = 1024 locations (1K)
Number of data lines = number of bits stored per location (word size)
Address lines (n) | Locations (2ⁿ)
8 | 256
10 | 1,024 (1K)
16 | 65,536 (64K)
20 | 1,048,576 (1M)
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
7
Notes: This is one of the most testable ideas in this whole topic, so let's slow down here. If a chip has n address pins, it can uniquely address 2 to the power n locations — because each address pin can independently be 0 or 1, giving you 2ⁿ combinations. So 10 address pins gives you 1024, or "1K," addressable locations. This is exactly how we talk about "1K x 8" or "4K x 4" memory chips — the first number is 2 raised to the number of address pins, and the second number is the number of data pins. Keep this formula in your notes; we'll use it constantly today.

## Slide 8
Notation — "Size × Width"
Chips are described as: Number of locations × Word size
Example: 1K × 8 means 1024 locations, each storing 8 bits
Total capacity (bits) = locations × word size = 1024 × 8 = 8192 bits = 1 KB
Address pins = log₂(locations) | Data pins = word size
1K
locations
×
8
bits wide
= 8,192 bits = 1 KB total
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
8
Notes: When you see a spec sheet say "1K by 8," don't panic — it's just telling you two numbers. The first number, before the "x," is how many separate storage locations exist. The second number, after the "x," is how wide each location is, in bits. So 1K x 8 has 1024 locations, each holding 8 bits, giving a total of 8192 bits, which conveniently works out to exactly 1 kilobyte. This notation is universal in datasheets, so getting comfortable reading it now will save you time later.

## Slide 9
Control Lines — CS, R/W, OE
Chip Select (CS): enables/disables the chip so several chips can share one bus
Read/Write (R/W): tells the chip to output data (read) or accept data (write)
Output Enable (OE): controls whether the data lines are actively driven
Together these let a system combine several small chips into one large memory
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
9
Notes: Address and data lines tell the chip "where" and "what," but control lines tell it "when" and "how." Chip Select is especially important — imagine you have four small chips, but only one system bus. Chip Select lets the system say "only you, chip number 2, should respond right now," while the other three stay silent. This is exactly how designers build large memory systems out of many smaller, cheaper chips, which we'll see in the next slide.

## Slide 10
Internal Organization — The Memory Array
Memory cells arranged in a 2D grid: rows and columns
Address is split into a row address and a column address
A decoder converts a binary address into "select exactly one row/column"
Intersection of selected row and column = the one cell (or word) being accessed
Row × Column → 1 cell
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
10
Notes: Now we go inside the chip. Instead of storing all locations in a single long line, designers arrange memory cells in a two-dimensional grid — this dramatically reduces the wiring complexity. To access one specific location, the incoming address is split into two parts: a row address and a column address. Each part goes into its own decoder, a circuit whose entire job is "given n input bits, activate exactly one of 2ⁿ output lines." The row decoder activates one row, the column decoder activates one column, and the single cell where they intersect is the one we're reading or writing.

## Slide 11
Row & Column Decoders — Step by Step
A decoder with n inputs has 2ⁿ outputs — exactly one active at a time
Example: a 3-to-8 decoder — 3 address bits select 1 of 8 rows
Splitting the address keeps decoders small (√N × √N instead of one 1-to-N decoder)
This is why memory arrays are often laid out as roughly square grids
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
11
Notes: Let's make the decoder idea concrete. A 3-to-8 decoder takes 3 input bits and produces 8 output lines, and for any given input combination, exactly one output line goes high — the rest stay low. Now here's the clever engineering trick: if you needed to select 1 of 1024 locations directly, you'd need a single decoder with 1024 output lines, which is a lot of circuitry. Instead, designers split the address in half — say 5 bits to a row decoder and 5 bits to a column decoder — giving 32 rows and 32 columns, whose intersection covers all 1024 locations, but using far fewer total decoder outputs. This is a big reason memory arrays are physically laid out as roughly square grids.

## Slide 12
Static vs Dynamic Memory Chips
SRAM: stores bits using flip-flops (~6 transistors); fast, no refresh needed
DRAM: stores bits as capacitor charge; needs periodic refreshing; denser and cheaper
SRAM → used in cache | DRAM → used in main memory
This tradeoff explains why cache is fast but small, and main memory is large but slower
SRAM
Flip-flop
(6T)
Fast
DRAM
Capacitor
(1T)
Dense
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
12
Notes: Here's a detail that directly connects to our cache discussion later. SRAM cells use flip-flop circuits — typically six transistors — to hold a bit stably as long as power is on, no refreshing needed, which makes SRAM fast but expensive and less dense. DRAM cells use just one transistor and a capacitor, which is much cheaper and denser, but the capacitor slowly leaks charge, so it must be refreshed thousands of times per second. This tradeoff is exactly why cache memory — which needs to be small and blazing fast — is built from SRAM, while main memory — which needs to be large and affordable — is built from DRAM.

## Slide 13
Memory Expansion — Combining Chips
Real systems need more memory than one chip provides
Wider word: connect chips side-by-side, same address lines, different data lines
More locations: connect chips using Chip Select lines with extra address bits
Example: four 1K×8 chips → 4K×8 memory using 2 extra address bits for chip selection
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
13
Notes: No single chip typically holds all the memory a computer needs, so designers combine multiple chips. There are two directions to expand in. To make a wider word — say from 8 bits to 32 bits — you connect four 8-bit chips in parallel, all sharing the same address lines, but each contributing its own 8 data lines. To make more locations — say combining four 1K-location chips into a 4K-location memory — you use two extra address bits to decide, through Chip Select, which one of the four chips is "listening" for that particular address. This is a very common exam question, so let's work through the numbers together in the next few slides.

## Slide 14
Worked Example — Combining Chips
Design an 8K×8 memory using 2K×8 chips. How many chips? How many extra address lines?
Step 1: Total locations needed = 8K = 8192; each chip gives 2K = 2048
Step 2: Number of chips = 8192 / 2048 = 4 chips
Step 3: Extra address bits for selection = log₂(4) = 2 bits
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
14
Notes: Let's solve this step by step, the way you would in an exam. We're told we need 8K by 8 total memory, built from 2K by 8 chips. First question: how many chips do we need? Just divide the total locations needed by what one chip provides — 8192 divided by 2048 gives us 4 chips. Second question: how many extra address bits do we need to pick which of those 4 chips is active? Since 4 equals 2 squared, we need exactly 2 extra address bits feeding a small 2-to-4 decoder, whose four outputs connect to the four chips' Chip Select pins. Notice the word size, 8 bits, didn't change at all here — because we're expanding locations, not word width.

## Slide 15
Real-World Example — Where This Shows Up
Your laptop's RAM modules are literally multiple DRAM chips combined this way
Embedded/robotics systems often combine small memory chips to save cost
Graphics cards use very wide memory buses (256-bit, 384-bit) built from many chips
Understanding chip organization helps you read a datasheet or a system spec
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
15
Notes: This isn't just theoretical. If you ever open up a laptop or look at a RAM stick, you'll see several small black rectangular chips on it — that's exactly the chip-combination idea from the last slide in action. In robotics projects, which connect directly to your department, you'll often see engineers combine small, cheap memory chips instead of buying one large expensive chip, precisely because of cost and availability. And in high-end GPUs, extremely wide memory buses are built by running many chips in parallel to move huge amounts of data per cycle. So this "boring" chip math directly explains hardware you interact with every day.

## Slide 16
Industry Example — Reading a Datasheet
Datasheets list: capacity (e.g. "256K × 16"), access time, pin diagram, voltage
Practice: given 256K × 16, find address lines, data lines, total capacity
Address lines = log₂(256K) = 18 | Data lines = 16
Total = 256K × 16 bits = 4 Mbits = 512 KB
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
16
Notes: Let's practice reading a real spec the way an engineer would. If a datasheet says "256K by 16," we can extract three facts instantly using what we've learned. Address lines: since 256K equals 2 to the 18th power, we need 18 address pins. Data lines: the word size is 16, so we need 16 data pins. Total capacity: multiply locations by width — 256K times 16 bits — which comes out to 4 megabits, or 512 kilobytes. Try pausing and working this out yourself before I reveal each answer — this exact skill of decoding a spec is genuinely useful, not just exam material.

## Slide 17
Transition — From Chips to Hierarchy
We now understand a single memory chip inside and out
Real systems use several levels: registers, cache, main memory, secondary storage
Why? Faster memory is always more expensive and smaller
This tradeoff is called the Memory Hierarchy
Registers
Cache
Main Memory
Secondary Storage
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
17
Notes: Good — we now understand how a single memory chip is organized internally, and how chips combine into larger memories. But here's the catch: if we built an entire computer's memory out of the fastest possible technology, it would be prohibitively expensive and physically difficult to make large. So real computer systems use a layered strategy called the memory hierarchy: tiny, extremely fast registers right inside the CPU; a small, fast cache just outside it; a much larger but slower main memory; and finally, a huge but comparatively very slow disk or SSD. This sets up exactly why cache memory exists — which is our focus for the rest of the hour.

## Slide 18
Why Cache Works — Principle of Locality
Temporal locality: a location accessed once is likely accessed again soon
Spatial locality: nearby locations are likely to be accessed soon too
Programs naturally show both — loops (temporal), array traversal (spatial)
Cache exploits locality by keeping recently/nearby-used data close to the CPU
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
18
Notes: Why does keeping a small amount of data "close by" even help? Because of a property almost all programs share, called locality of reference, and it comes in two flavors. Temporal locality means if you used a piece of data once, you're likely to use it again very soon — think of a loop variable that gets checked every iteration. Spatial locality means if you accessed one memory location, you're likely to access nearby locations soon too — think of scanning through an array element by element. Cache memory is designed specifically to exploit both of these patterns, which is why it works so well in practice even though it's much smaller than main memory.

## Slide 19
What Is Cache Memory, Structurally?
Divided into fixed-size lines/blocks (e.g. 32 or 64 bytes each)
Each line stores: data, a tag (identifies the source block), and a valid bit
On a CPU request, cache checks: "Do I have this address's data?" → Hit or Miss
A cache hit is fast; a cache miss requires fetching from slower main memory
Valid
Tag
Data
One cache line
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
19
Notes: Structurally, cache is organized into fixed-size chunks called lines or blocks — commonly 32 or 64 bytes. Each line stores three things: the actual copied data, a tag that records which specific block of main memory this data came from, and a valid bit that says whether this line currently holds meaningful data at all. When the CPU asks for a memory address, the cache controller checks whether it already holds the relevant block — if yes, that's a cache hit, and data comes back almost instantly; if no, that's a cache miss, and the system has to go all the way to main memory, which is much slower. Cache mapping techniques, which we cover next, are exactly the rules for where a given main memory block is allowed to be placed within the cache.

## Slide 20
Address Breakdown — Tag, Index, Offset
Offset: which byte within the block (depends on block size)
Index/Line: which cache line this address could map to (depends on mapping type)
Tag: remaining bits, stored to verify a match
Offset bits = log₂(block size)
Tag
Index
Offset
32-bit memory address
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
20
Notes: Every cache lookup starts by slicing the incoming memory address into three pieces. The offset — the rightmost bits — tells us which specific byte within a block we want; its size is determined entirely by the block size, since log base 2 of the block size gives the number of offset bits. The index, sometimes called the line number, tells the hardware which cache line to check — this piece only exists for direct-mapped and set-associative caches, as we'll see. And the tag — the remaining, leftmost bits — is stored alongside the data specifically so the cache can verify "is this really the block I think it is." Keep this three-part breakdown in mind; it's the backbone of every cache mapping numerical you'll solve.

## Slide 21
Mapping Technique 1 — Direct Mapping
Each main memory block maps to exactly one cache line
Line = Block number MOD number of cache lines
Simple hardware, very fast lookup
Drawback: two blocks sharing a line evict each other repeatedly ("thrashing")
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
21
Notes: The simplest mapping strategy is direct mapping. Here, every block of main memory has exactly one, fixed cache line it's allowed to live in — determined by taking the block number modulo the total number of cache lines. This makes direct mapping wonderfully simple and fast in hardware, because there's no searching involved; you compute one index and check one line. But it has a real weakness: if a program happens to alternate between two blocks that map to the same line, the cache will constantly evict one to bring in the other, even if every other cache line is sitting empty. This repeated back-and-forth eviction is called thrashing, and it's the main motivation for the next two techniques.

## Slide 22
Mapping Technique 2 — Fully Associative
A memory block can go into any cache line — no fixed rule
No index bits needed — the entire address (minus offset) is the tag
Requires checking all tags in parallel (a comparator per line)
Very flexible, but expensive and power-hungry for large caches
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
22
Notes: At the opposite extreme is fully associative mapping, where a memory block can be placed in absolutely any cache line — there's no fixed rule at all. Because there's no index needed, essentially the entire address, apart from the offset, becomes the tag. The tradeoff is in hardware complexity: to find whether a block is present, the cache must compare the incoming tag against every single line's tag simultaneously, which needs a dedicated comparator per line. This gives excellent flexibility and minimizes thrashing, but it's expensive in silicon and power, so it's typically only used for small, specialized caches.

## Slide 23
Mapping Technique 3 — Set-Associative
A compromise between direct and fully associative
Cache divided into sets, each containing k lines ("k-way set associative")
A block maps to exactly one set, but any line within that set
Common in real CPUs: 4-way, 8-way, 16-way set-associative caches
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
23
Notes: Set-associative mapping is the practical middle ground that most real CPUs actually use. The cache is divided into groups called sets, and each set contains a small fixed number of lines — say 4, giving us "4-way set associative." A memory block is still restricted to exactly one set, computed the same way as direct mapping, but within that set, it can occupy any of the available lines, just like fully associative mapping. This gives most of the thrashing-resistance benefit of full associativity, while keeping the hardware comparator cost manageable, since you only need to compare against the handful of lines within one set, not the whole cache. This is why you'll commonly hear real processors described as having "8-way set-associative L1 cache," for example.

## Slide 24
Comparing the Three Techniques
Technique | Placement Flexibility | Hardware Cost | Thrashing Risk
Direct Mapped | 1 specific line | Lowest | Highest
Fully Associative | Any line | Highest | Lowest
Set-Associative | Any line within 1 set | Moderate | Moderate
Set-associative caching is the most common choice in real processors because it balances all three dimensions.
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
24
Notes: Let's consolidate what we just covered into one comparison. Direct mapping gives you the least flexibility but the cheapest, fastest hardware, and the highest chance of thrashing. Fully associative mapping gives maximum flexibility and the lowest thrashing risk, but at the highest hardware cost. Set-associative mapping sits in between on every single dimension — which is exactly why it's the most commonly used approach in real, modern processors. If an exam asks you to justify why set-associative caches are popular, this tradeoff table is your answer.

## Slide 25
Worked Numerical — Direct Mapping
Main memory = 4096 blocks; Cache = 128 lines (direct mapped)
Which cache line does block number 260 map to?
Line = Block number MOD number of cache lines
Line = 260 MOD 128 = 4 → Block 260 maps to cache line 4
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
25
Notes: Let's apply direct mapping to real numbers. We're told main memory has 4096 blocks and cache has 128 lines, direct mapped, and we want to know where block 260 lands. The rule for direct mapping is always the same: take the block number modulo the number of cache lines. So 260 mod 128 — 128 goes into 260 once with remainder 132, then 128 goes into 132 once more with remainder 4. So 260 mod 128 equals 4, meaning block 260 always maps to cache line number 4, no matter what — and note that block 4, block 132, block 260, block 388, and so on, all compete for that exact same line 4.

## Slide 26
Worked Numerical — Address Bit Breakdown
32-bit address, direct-mapped cache = 64 KB, block size = 32 bytes
Offset bits = log₂(32) = 5
Lines = 64KB / 32B = 2048 → Index bits = log₂(2048) = 11
Tag bits = 32 − (11 + 5) = 16
Tag
16b
Index
11b
Off
5b
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
26
Notes: This is the classic cache numerical, so let's go carefully. We have a 32-bit address, a direct-mapped cache of 64 kilobytes, and a block size of 32 bytes. First, the offset: since each block holds 32 bytes, we need log base 2 of 32, which is 5 offset bits, to select a byte within a block. Next, the index: the total number of lines equals cache size divided by block size — 64 kilobytes divided by 32 bytes gives 2048 lines — and log base 2 of 2048 is 11 index bits. Finally, whatever bits remain from the full 32-bit address become the tag: 32 minus 11 minus 5 gives us 16 tag bits. So our final address breakdown is 16 bits of tag, 11 bits of index, and 5 bits of offset — and this exact style of problem, just with different numbers, shows up constantly in exams.

## Slide 27
Worked Numerical — Set-Associative Mapping
Cache has 256 lines, 4-way set-associative
How many sets? How many index bits?
Sets = Total lines / Ways = 256 / 4 = 64 sets
Index bits = log₂(64) = 6 (tag still compared against all 4 lines in the set)
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
27
Notes: One more numerical, this time for set-associative mapping. We're told the cache has 256 total lines arranged as 4-way set-associative — meaning each set contains 4 lines. To find the number of sets, divide total lines by the number of ways: 256 divided by 4 gives us 64 sets. The index field only needs to identify which set, not which exact line, so we take log base 2 of 64, giving us 6 index bits. Once the correct set is located using those 6 bits, the hardware then compares the tag against all 4 lines within that one set in parallel — that parallel comparison within a small set, rather than the whole cache, is exactly what keeps set-associative caches affordable.

## Slide 28
Common Misconceptions & Pitfalls
"Bigger cache always means proportionally faster" — depends on locality of access
"Fully associative is always best" — most flexible, but not most cost-effective at scale
Pitfall: offset bits depend on block size, not cache size
Pitfall: confusing "line/block number" with "byte address" in calculations
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
28
Notes: Before we wrap up the core content, let's flag a few traps students commonly fall into. First, don't assume a bigger cache automatically makes everything faster — the actual benefit depends heavily on whether the program's access pattern has good locality; a program that jumps around memory unpredictably won't benefit as much. Second, don't assume fully associative caching is simply "the best" — yes, it minimizes thrashing, but the hardware cost usually makes it impractical for large caches, which is exactly why set-associative won out in practice. And in your numericals, the single most common calculation mistake is confusing the offset bit-width, which comes from block size, with the index bit-width, which comes from cache size — keep those formulas straight.

## Slide 29
Mini Activity — Quick Check
In pairs: A cache has 32 lines, direct mapped.
Which line does block number 100 map to?
Hint: use the modulo rule. | Take 90 seconds.
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
29
Notes: Let's do a quick, low-stakes check before we move to the summary. Pair up with the person next to you and work out: with 32 direct-mapped cache lines, where does block number 100 land? Give them about ninety seconds. [After time is up] Let's check together: 100 mod 32 — 32 goes into 100 three times, using 96, with a remainder of 4 — so block 100 maps to cache line 4. If your pair got that, great, you've got the core mechanic down. If not, no worries — that's exactly why we're reviewing it now, before the graded quiz.

## Slide 30
Summary of Key Points
Memory chips: n address lines → 2ⁿ locations; capacity = locations × word size
Chips combine via shared address lines (wider word) or Chip Select (more locations)
Cache exploits temporal & spatial locality to bridge the CPU–memory speed gap
Three mapping techniques: Direct (1 line), Fully Associative (any line), Set-Associative
Address splits into Tag + Index + Offset for every cache lookup
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
30
Notes: Let's tie everything together. We started inside a single memory chip, learning that address pins determine capacity through the 2 to the n relationship, and that real systems combine multiple chips either to widen the data word or to add more addressable locations using Chip Select. Then we zoomed out to see why cache memory exists at all — because of the enormous speed gap between CPUs and main memory, and because programs naturally reuse the same and nearby data. Finally, we worked through the three cache mapping techniques and practiced splitting addresses into tag, index, and offset by hand. All of this comes together in the quiz next, so take a breath, and let's test your understanding.

## Slide 31
Quiz — Memory Chips & Cache Mapping
Q1. A chip has 12 address lines. How many locations can it address? (a) 1024 (b) 2048 (c) 4096 (d) 8192
Q2. True/False: Fully associative mapping requires index bits to locate a cache line.
Q3. In a "2K × 16" chip, how many data lines are needed? (a) 8 (b) 11 (c) 16 (d) 2048
Q4. In one sentence: why is set-associative mapping a compromise between direct and fully associative?
Q5. A cache has 512 lines, 8-way set associative. How many sets exist? (a) 32 (b) 64 (c) 128 (d) 512
Q6. True/False: Offset bit-width depends on cache size, not block size.
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
31
Notes: Give students 4 to 5 minutes to attempt this individually — remind them this is a self-check, not for grading, so honest effort matters more than getting every answer right. Q1 and Q3 directly test the address-line and data-line formulas from slides 7 to 8. Q2 and Q6 test conceptual understanding from slides 20 to 22 — watch for students confusing "no index needed" with "no lookup needed" in Q2. Q4 tests whether students can explain set-associative mapping in their own words, tying back to slide 24's comparison table. Q5 is a direct numerical, same style as slide 27's worked example. After time is up, move to the next slide and reveal answers together.

## Slide 32
Quiz Answers — Memory Chips & Cache Mapping
A1. (c) 4096 — because 2¹² = 4096
A2. False — fully associative needs no index; the whole address (minus offset) is the tag
A3. (c) 16 — the "16" in "2K × 16" is the word size, which equals the number of data lines
A4. It restricts a block to one set (like direct) but allows any line within that set (like fully associative)
A5. (b) 64 — since 512 ÷ 8 = 64 sets
A6. False — offset bit-width depends on block size (log₂ of block size), not cache size
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
32
Notes: Let's go through these quickly. Q1: 2 to the 12 is 4096, so (c) is correct — a very common mistake here is students accidentally computing 12 times 2 instead of 2 to the power 12, so flag that if you see it. Q2: false, and this is the single most-missed concept — many students think "fully associative" means "no lookup at all," when really it means "check everywhere," which is actually more comparator work, not less. Q3: (c) 16, straight from the "size x width" notation. Q4 is open-ended; accept any answer that captures the "restricted set, flexible line within it" idea. Q5: 512 divided by 8 is 64 sets — a direct application of slide 27's method. Q6: false — remind students this offset-versus-index mix-up is the number one calculation error in this topic, so it's worth re-reading slide 20 tonight if they got this wrong.

## Slide 33
Further Reading & What's Next
Recommended: Cache write policies — Write-Through vs Write-Back (next topic)
Recommended: Cache replacement policies — LRU, FIFO, Random (next topic)
Practice: attempt 5 more cache-mapping numericals from the course problem set
Next lecture: Cache Performance — Hit Ratio, Average Memory Access Time (AMAT)
Presidency University | Department of AI & Robotics | CSS2257 | Computer Organization and Architecture
33
Notes: Before we close, a quick look ahead. Today we focused on where a block gets placed in cache — the mapping techniques. What we haven't covered yet, and will next time, is what happens when we write to cache — the write-through versus write-back policies — and what happens when the cache is full and something has to be evicted, which is where replacement policies like LRU come in. For practice before then, I'd like you to attempt five more mapping numericals from the problem set; the pattern is always the same three steps we used today. Thank you all for a great session — see you next class for cache performance metrics.