## Slide 1
Presidency University | CSS2257 | Computer Organization and Architecture
Presidency University
Cache Mapping: Tag, Index and Word Fields
Computer Organization and Architecture | CSS2257
School of Artificial Intelligence and Advanced Computing
Department of AI & Robotics
Faculty: Manoj Sagar
Tag
Index
Word
Notes: Welcome the class. Today we solve one classic cache problem three ways: direct, fully associative and 4-way set-associative. The main memory and cache never change; only the way an address is split changes. By the end, students should split any address in under a minute.

## Slide 2
Learning Objectives
Presidency University | CSS2257 | Computer Organization and Architecture
Explain lines, blocks, tag, index and word offset
Compute the word offset from block size
Find Tag, Line/Set and Word bits for three mappings
Compare the mappings and avoid common slips
Notes: Read the four outcomes. Tell students the worked problem has three parts and each part needs only powers of two and subtraction. Assure them nothing here needs a calculator.

## Slide 3
Icebreaker: Warm-up Questions
Presidency University | CSS2257 | Computer Organization and Architecture
1
Why does a website open faster the second time you visit it?
2
In a library, how do 'row, shelf, book' pick one book quickly?
3
If 512 lockers serve 32,768 students, who decides which locker you use?
Notes: Show of hands, 3 minutes. Q1: a library shelf label such as 'Row 4, Shelf 2, Book 7' is exactly tag, index and offset. Q2: browsers cache pages so repeat visits load faster. Use answers to introduce why a cache must quickly recognise which block it holds.

## Slide 4
Cache Basics: Vocabulary
Presidency University | CSS2257 | Computer Organization and Architecture
Block: chunk of words copied from memory to cache
Line: one cache slot that holds one block
Tag: identifies which block is in the line
Hit: tag matches; Miss: fetch block from memory
Real example: CPU L1 cache, browser cache
Notes: Define each term with the library example. A block is the unit copied from main memory into a cache line. The tag says WHICH memory block currently sits in the line, since many blocks compete for one line. A hit means the tag matches; a miss means we fetch the block from memory.

## Slide 5
Address Split: Tag | Index | Word
Presidency University | CSS2257 | Computer Organization and Architecture
A19
A0
Tag = 8
Line / Set = 7
Word = 5
Word bits = log₂(words per block)
Line bits = log₂(lines); Set bits = log₂(sets)
Tag bits = address − index − word
Notes: Every mapping cuts the 20-bit address into fields. Word offset picks a word inside the block. Index (line or set) picks where to look in the cache. Tag is whatever remains, used for comparison. Rule: tag = address bits minus index bits minus word bits.

## Slide 6
The Problem and Step 1: Word Offset
Presidency University | CSS2257 | Computer Organization and Architecture
Address = 20 bits → 2²⁰ words
Memory = 32K = 2¹⁵ blocks
Cache = 512 = 2⁹ lines, 32 words per line
1
Words per block = 2²⁰ ÷ 2¹⁵ = 2⁵ = 32
2
Word offset = log₂ 32 = 5 bits (same for all mappings)
Notes: Read the problem. Step 1 is common to all three mappings. Address has 20 bits so memory has 2 to the 20 words. It has 32K equals 2 to the 15 blocks, so each block holds 2 to the 5 equals 32 words. This agrees with the cache line size of 32 words. So the word offset is 5 bits, always.

## Slide 7
1. Direct Mapping: 6 | 9 | 5
Presidency University | CSS2257 | Computer Organization and Architecture
A19
A0
Tag = 6
Line = 9
Word = 5
1
Line bits = log₂ 512 = 9
2
Tag bits = 20 − 9 − 5 = 6
Notes: Each memory block maps to exactly one line: line number equals block number modulo 512. So we need log2 512 equals 9 line bits. Tag is 20 minus 9 minus 5 equals 6. Check: 2 to the 15 blocks divided by 512 lines gives 64 blocks per line, and 64 needs 6 tag bits. Animation: reveal fields one by one.

## Slide 8
2. Fully Associative Mapping: 15 | 5
Presidency University | CSS2257 | Computer Organization and Architecture
A19
A0
Tag = 15
Word = 5
1
Index bits = 0 (block can sit in any line)
2
Tag bits = 20 − 5 = 15 (the full block number)
3
Trade-off: 512 comparators, no conflict misses
Notes: A block may go in any line, so there is no index field at all. The whole block number must be stored as the tag: 20 minus 5 equals 15 bits. Cost: the cache must compare the incoming tag with all 512 stored tags in parallel, which needs more hardware.

## Slide 9
3. 2-Way Set-Associative: 7 | 8 | 5
Presidency University | CSS2257 | Computer Organization and Architecture
A19
A0
Tag = 7
Set = 8
Word = 5
1
Sets = 512 ÷ 2 = 256 = 2⁸ → Set bits = 8
2
Tag bits = 20 − 8 − 5 = 7
3
Only 2 comparators per lookup
Notes: Group the 512 lines into sets of 2. Number of sets equals 512 divided by 2 equals 256, which is 2 to the 8, so 8 set bits. A block maps to one set but can use either of its 2 lines. Tag is 20 minus 8 minus 5 equals 7. Only 2 comparators are needed per lookup. Animation: reveal fields one by one.

## Slide 10
4. 4-Way Set-Associative: 8 | 7 | 5
Presidency University | CSS2257 | Computer Organization and Architecture
A19
A0
Tag = 8
Set = 7
Word = 5
1
Sets = 512 ÷ 4 = 128 = 2⁷ → Set bits = 7
2
Tag bits = 20 − 7 − 5 = 8
3
Only 4 comparators per lookup
Notes: Group the 512 lines into sets of 4. Number of sets equals 512 divided by 4 equals 128, which is 2 to the 7, so 7 set bits. A block maps to one set but can use any of its 4 lines. Tag is 20 minus 7 minus 5 equals 8. Note the tag sits between the direct and fully associative values.

## Slide 11
Comparison of the Three Mappings
Presidency University | CSS2257 | Computer Organization and Architecture
Mapping | Tag | Line / Set | Word
Direct | 6 | 9 (line) | 5
Fully associative | 15 | 0 | 5
2-way set-associative | 7 | 8 (set) | 5
4-way set-associative | 8 | 7 (set) | 5
Each row sums to 20 bits
Notes: Read down each column. The word field is fixed at 5. As associativity grows, index bits shrink and tag bits grow, since more blocks share fewer index positions. Direct has the fewest tag bits and simplest hardware; fully associative has the most flexibility and the largest tags.

## Slide 12
Practice Problem
Presidency University | CSS2257 | Computer Organization and Architecture
A19
A0
Tag = 8
Set = 7
Word = 5
1
Sets = 512 ÷ 4 = 128 = 2⁷ → Set bits = 7
2
Tag bits = 20 − 7 − 5 = 8
3
Only 4 comparators per lookup
Notes: Group the 512 lines into sets of 4. Number of sets equals 512 divided by 4 equals 128, which is 2 to the 7, so 7 set bits. A block maps to one set but can use any of its 4 lines. Tag is 20 minus 7 minus 5 equals 8. Note the tag sits between the direct and fully associative values.

## Slide 13
Common Mistakes
Presidency University | CSS2257 | Computer Organization and Architecture
Word bits come from block size, not cache size
Sets = lines ÷ ways (512 ÷ 4 = 128, not 512)
Fully associative has NO index field
Always check: Tag + Index + Word = 20
Notes: Go through each slip. Students often forget that word offset comes from block size, not cache size. Another slip is using 512 instead of 128 for the set count. A third is giving fully associative an index field. Encourage them to always check that the fields add to 20.

## Slide 14
Quick Check: 8-Way Set-Associative
Presidency University | CSS2257 | Computer Organization and Architecture
1
Sets = 512 ÷ 8 = 64 → 6 set bits
2
Word = 5 bits (unchanged)
3
Tag = 20 − 6 − 5 = 9 bits
Notes: Let students work it out for 2 minutes. Sets equal 512 divided by 8 equals 64, which is 2 to the 6, so 6 set bits. Word stays 5. Tag equals 20 minus 6 minus 5 equals 9. Notice the trend: doubling ways removes one index bit and adds one tag bit.

## Slide 15
Summary
Presidency University | CSS2257 | Computer Organization and Architecture
Word offset = 5 bits for every mapping
Direct: Tag 6, Line 9, Word 5
Fully associative: Tag 15, Word 5
2-way: Tag 7, Set 8, Word 5
4-way: Tag 8, Set 7, Word 5
Notes: Recap in one minute: the offset is fixed at 5, the index depends on lines or sets, and the tag is the remainder. Answers: direct 6, 9, 5; fully associative 15, 0, 5; 2-way 7, 8, 5; 4-way 8, 7, 5. The quiz comes next as a self-check.

## Slide 16
Quiz: Cache Mapping (CSS2257)
Presidency University | CSS2257 | Computer Organization and Architecture
Q1. Words per block if memory has 2²⁰ words in 2¹⁵ blocks?
Q2. Word offset bits for a 32-word block?
Q3. Direct mapping with 512 lines: index bits?
Q4. True/False: fully associative mapping has an index field.
Q5. Number of sets in a 4-way cache with 512 lines?
Q6. Tag bits for a 16-way cache (same memory and cache)?
Notes: Give 3 minutes, individually or in pairs. Q1 and Q2 test the fixed offset, Q3 and Q4 test direct and associative fields, Q5 tests set count, Q6 tests the trend. Say clearly that this is a self-check. Animation: reveal questions one by one.

## Slide 17
Quiz Answers
Presidency University | CSS2257 | Computer Organization and Architecture
A1. 32 words (2⁵).
A2. 5 bits.
A3. 9 bits (log₂ 512).
A4. False: index = 0, tag = 15.
A5. 128 sets (512 ÷ 4).
A6. Sets = 512 ÷ 16 = 32 → 5 bits; Tag = 20 − 5 − 5 = 10.
Notes: Go through each answer. For Q4, remind students that with no index the entire block number is the tag. For Q6: sets equal 32, which is 5 bits, so tag equals 20 minus 5 minus 5 equals 10, continuing the trend. Ask students to note anything tricky for revision. Animation: reveal answers one by one.