## Slide 1
Presidency University | CSS2257 | Computer Organization and Architecture
Presidency University
Internal Organization of 16 × 8 and 16 × 4 Memory Chips
Computer Organization and Architecture | CSS2257
School of Artificial Intelligence and Advanced Computing
Department of AI & Robotics
Faculty: Manoj Sagar
Notes: Welcome the class. Today we open up a memory chip and look inside: how an address picks one word, and how many bits come out. We compare two chips with the same number of words but different word widths. Take 1 minute to set expectations: by the end, everyone should be able to draw both chips.

## Slide 2
Learning Objectives
Presidency University | CSS2257 | Computer Organization and Architecture
Define word, bit, capacity and address lines
Draw the internal organization of a 16 × 8 chip
Draw the 16 × 4 chip and compare the two
Combine chips to build wider or deeper memory
1
Know
2
Draw
3
Compare
4
Build
Notes: Read the four outcomes aloud. Stress that we will move from definitions to a diagram to a small design problem. Tell students the quiz at the end mirrors these four outcomes exactly.

## Slide 3
Icebreaker: Warm-up Questions
Presidency University | CSS2257 | Computer Organization and Architecture
1
Your phone says 128 GB. How many separate storage cells do you think that is?
2
How does a chip find ONE location among millions?
3
If a street has 16 houses, how many bits do you need to number them?
Notes: Run this as a show of hands, 3 minutes total. Take two or three quick answers per question. Q1: a phone with 8 GB has billions of tiny storage cells. Q2: the address is like a house number. Use their answers to lead into 'how does a chip find one word among many?'

## Slide 4
Words, Bits and Capacity
Presidency University | CSS2257 | Computer Organization and Architecture
Bit: one binary digit (0 or 1)
Word: bits accessed together in one operation
Capacity = number of words × bits per word
Example: 16 × 8 → 16 words of 8 bits = 128 bits
1
0
1
1
0
0
1
0
1 word = 8 bits
128 bits
16 words × 8 bits
Notes: A bit stores 0 or 1. A word is a group of bits that is read or written together. Example: a chip with 16 words of 8 bits holds 16 × 8 = 128 bits. Ask: what would 16 words of 4 bits hold? Let them answer 64 bits before you reveal it.

## Slide 5
Address Lines: Choosing One Word
Presidency University | CSS2257 | Computer Organization and Architecture
n address lines select 2ⁿ words
16 words → n = 4 (A3 A2 A1 A0)
32 words → 5 lines; 1024 words → 10 lines
Word width does NOT change the address lines
2⁴ = 16
4 address lines → 16 words
Same for both
16 × 8 and 16 × 4 need A3–A0
Notes: With n address lines we can name 2 to the power n words. Sixteen words need 4 lines because 2 to the 4 is 16. Both of our chips have 16 words, so both use A3 to A0. Check understanding: how many lines for 1024 words? Ten.

## Slide 6
16 × 8 Chip: Internal Organization
Presidency University | CSS2257 | Computer Organization and Architecture
4-to-16
Decoder
A3
A2
A1
A0
W0
W1
⋮
W15
Sense/Write
R/W, CS
D7 … D0 (8 data lines)
128 cells
16 rows × 8 columns
14 connections
4 address + 8 data + 2 control
(plus power and ground)
Notes: Walk left to right. The 4-bit address enters the decoder, which raises exactly one of 16 word lines. Each word line selects a row of 8 cells. Below the array, 8 sense/write circuits connect the 8 columns to the data lines D7 to D0. R/W and CS control the operation. Animation: fade in address, decoder, word lines, array, then sense/write.

## Slide 7
16 × 4 Chip: Internal Organization
Presidency University | CSS2257 | Computer Organization and Architecture
4-to-16
Decoder
A3
A2
A1
A0
W0
W1
⋮
W15
Sense/Write
R/W, CS
D3 … D0 (4 data lines)
64 cells
16 rows × 4 columns
10 connections
4 address + 4 data + 2 control
(plus power and ground)
Notes: Same decoder, same 16 word lines, but each row now has only 4 cells. So the array is half as wide and only 4 sense/write circuits are needed. Ask students what changed: data lines drop from 8 to 4, storage drops from 128 to 64 bits. Address lines stay at 4.

## Slide 8
16 × 8 vs 16 × 4 at a Glance
Presidency University | CSS2257 | Computer Organization and Architecture
Feature | 16 × 8 | 16 × 4
Words | 16 | 16
Bits per word | 8 | 4
Capacity | 128 bits | 64 bits
Address lines | 4 | 4
Data lines | 8 | 4
Sense/write circuits | 8 | 4
External connections | 14 | 10
Notes: Read across each row. Only the width-dependent items change: bits per word, data lines, cells, sense/write circuits and pin count. Words and address lines stay the same. This is the key insight of the lecture.

## Slide 9
How a Read or Write Works
Presidency University | CSS2257 | Computer Organization and Architecture
1
Place address on A3–A0
→
2
Decoder raises ONE word line
→
3
Set R/W (1 = read, 0 = write) and CS = 1
→
4
Sense/write circuits move the word's bits
Example: address 0101 → word line W5 → 8 bits on D7–D0
Notes: Trace one read: address 0101 arrives, the decoder raises W5, the 8 cells in row 5 drive their bit lines, the sense circuits detect them, and the 8 bits appear on D7 to D0. For a write, the sense/write circuits drive the bit lines instead and the row stores the new values. Animation: highlight each box as you speak.

## Slide 10
Real-World Connections
Presidency University | CSS2257 | Computer Organization and Architecture
1
DRAM chip widths
Chips come as x4, x8, x16: bits delivered per access
2
Memory module
Eight x8 chips side by side → 64-bit data bus
3
Cache and register file
Decoder + cell array, same principle, on the CPU die
Notes: Real DRAM chips are sold in x4, x8 and x16 widths, which is exactly the 'bits per word' idea. A memory module puts several chips side by side so their data lines together form a 64-bit bus. Register files and caches use the same decoder plus array structure on-chip.

## Slide 11
Worked Example: Two 16 × 4 → One 16 × 8
Presidency University | CSS2257 | Computer Organization and Architecture
16 × 4 chip 1
16 × 4 chip 2
A3–A0
R/W, CS
(shared)
D7–D4
D3–D0
Result: 16 words × 8 bits = 128 bits
Notes: Width expansion. Both chips get the same address, CS and R/W, so they select the same row together. Chip 1 supplies the upper four data bits and chip 2 the lower four. Together they behave as one 16 by 8 memory. Ask: how many address lines? Still four.

## Slide 12
Worked Problem: Build 64 × 8 from 16 × 4 Chips
Presidency University | CSS2257 | Computer Organization and Architecture
1
Total bits: 64 × 8 = 512; chip = 64 → 8 chips
2
Width: 8 ÷ 4 = 2 chips per row
3
Depth: 64 ÷ 16 = 4 rows of chips
4
64 words → 6 address lines: A3–A0 to all chips; A5–A4 → 2-to-4 decoder → CS of each row
Notes: Step 1: total bits 64 times 8 is 512; each chip holds 64, so 8 chips. Step 2: width 8 divided by 4 gives 2 chips per row. Step 3: depth 64 divided by 16 gives 4 rows. Step 4: 64 words need 6 address lines; A3 to A0 go to every chip, A5 and A4 feed a 2-to-4 decoder that drives the chip selects of the 4 rows. Walk slowly and let students compute each step first.

## Slide 13
Summary
Presidency University | CSS2257 | Computer Organization and Architecture
Address lines = log₂(words) → 4 for both chips
Bits per word set data lines and sense/write circuits
16 × 8 = 128 bits (14 connections); 16 × 4 = 64 bits (10)
Chips combine for wider words or more words
Notes: Recap in one minute. Words fix the address lines; bits per word fix the data lines, the sense/write count and the pin count. Chips combine in width for wider words and in depth for more words. Tell students the quiz is next and is for self-check only.

## Slide 14
Quiz: Memory Chip Organization (CSS2257)
Presidency University | CSS2257 | Computer Organization and Architecture
Q1. Capacity of a 16 × 8 chip in bits?
Q2. Address lines needed for 16 words?
Q3. Data lines on a 16 × 4 chip?
Q4. True/False: a 16 × 4 chip needs fewer address lines than 16 × 8.
Q5. Sense/write circuits in a 16 × 8 chip?
Q6. Chips of 16 × 4 needed to build 32 × 8?
Notes: Give students 3 minutes, individually or with a neighbour. Q1 to Q3 test capacity and lines, Q4 tests the key misconception, Q5 links to the diagram, Q6 needs width and depth reasoning. Say clearly this is a self-check, not graded. Animation: reveal questions one by one.

## Slide 15
Quiz Answers
Presidency University | CSS2257 | Computer Organization and Architecture
A1. 128 bits (16 × 8).
A2. 4 lines, since 2⁴ = 16.
A3. 4 data lines (D3–D0).
A4. False: both use 4; width does not matter.
A5. 8, one per column.
A6. 4 chips: 2 wide × 2 deep.
Notes: Go through each answer briefly. For Q4, restate that address lines depend only on the number of words. For Q6, show the width step (16 × 4 twice for 8 bits) and the depth step (two rows for 32 words). Ask students to note anything tricky for revision. Animation: reveal answers one by one.